## Slide 1: Karabo goes AMQP: Replacement of the Core Communication Broker
Dr. Gero Flucke
for the Controls group @ European XFEL GmbH
September 25th, 2024

## Slide 2: Outline
Karabo Communication Basics
Struggles with the original JMS broker implementation
Refactoring Strategy
Timeline
  Refactoring
  Deployment
  Issues on the way
Summary
Karabo: Supervisory Control and Data Acquisition at the beamlines and instruments of the
European XFEL (Hamburg Metropolitan Area)

## Slide 3: Karabo: Device Based Communication via a Message Broker
Self-describing Karabo Devices
Equipment control, e.g. motors, valves,…
Detectors
  e.g. cameras
Online data analysis
Data Logging
Other system services
  GUI entry point
  DAQ for big/scientific data (not shown)
Message Broker
Equipment
Control
e.g. motor, pump, valve, sensor
DAQ
Equipment
e.g. commercial camera
GUI Server
and other service devices like configuration manager
Analysis
Node
e.g. calibration, image processing
Data Logging
Node
storage of control data and configurations
Command Line
Interface
Graphical
User Interface
Interface for Users and Operators
TCP/IP data pipelines for
big/fast data

## Slide 4: Karabo Communication Patterns
1-to-1: Request and reply
  Device registers methods as “slots”.
  Request from remote with up to four arguments
    Reply if done with up to four values.
    Requester can suppress reply (fire-and-forget)
1-to-all: Broadcast (for system purpose only)
  Always fire-and-forget
  Still costly, so used rarely:
    System topology: instance new and gone
    Problematic device states (UNKNOWN, ERROR)
Device2
Device1
Request
slot
Notify
Notify
Reply
Device1
Device2
Device3
Device4
Call slot
Notify
Notify
Notify
DeviceN
Notify
…
Notify

## Slide 5: Karabo Communication Patterns (ctd.)
Publish/subscribe
  Devices (2 & 5) subscribe slots to a remote “signal”.
  When signal is “emitted”, all subscribed slots are called.
    No publishing overhead for “popular” devices
    Karabo framework is completely event-driven: regular polling obsolete.
Device1
Device2
Device3
Device4
Emit
signal
Notify
Device5
Notify

## Slide 6: Karabo APIs
C++:
  “First language” of Karabo
  High performance framework devices (GUI server, data logging) and digitizers, some cameras
Python “Bound”:
  Python bindings on top of C++ (now using pybind11)
    Communication completely covered by C++
  Many similarities with C++  not very Pythonic
Python “Middlelayer” (MDL):
  Pure Python (early use of asyncio library, single thread)
  Nowadays most popular API, not only for middlelayer devices
Karabo installation size e.g. about:
2700 devices
400 k properties
1.2 kHz message rate to broker
4.3 kHz message rate from broker
(13 such installations at EuXFEL)

## Slide 7: Original Karabo Broker Implementation
Broker: Java Messaging System (JMS) – OpenMQ
Client library: OpenMQc
  C/C++ library also directly called from pure Python API (MDL)
Each device subscribes once to a Karabo “topic” (e.g. for one of the EuXFEL instruments)
  Broker filters messages according to target device ids in message header
    message header carries target information
    signal subscription not on the broker, but on Karabo device emitting the signal
Device1
Device2
Device3
Device4
Emit
signal
Notify
Device5
Notify

## Slide 8: Problems with JMS Broker and OpenMQc Library
Global message backlog
  Messages not consumed kept on broker
    If max. reached, broker refuses messages:
      No communication anymore!
  Causes:
    Badly behaving processes
    Many receivers in one process
Message drop
  Hacked into the code as last rescue
  Triggered memory leak in OpenMQc
OpenMQc library not maintained
  Memory leak problem fixed only four years after we reported in 2015
4 Hz
10 Hz
1 Hz
Rates: all 370 receivers
Problems worked around over years:
  Except backlog from badly behaving processes
    Closely monitoring backlog
    On-call staff hunting process to kill
    Failed very few times per year
      (potential loss of few hours of beamtime)

## Slide 9: Refactoring Strategy I
Broker communication is critical:
  Need to be able to switch back to old broker at any time
    Allow switching back and forth by just changing the environment variable $KARABO_BROKER
Introduce abstract base class for broker communication (both APIs: C++ and MDL)
  Concrete class for each broker protocol supported
  Dynamically choose concrete class according to protocol part of broker address
    tcp://somehost:7777 - tcp  JmsBroker
    amqp://anotherhost:5672 – amqp  AmqpBroker
    …
Long timeline of project:
  No long lived feature branch in git (fear of divergence)
  But merge smaller changes
    always keeping JMS communication intact

## Slide 10: Refactoring Strategy II
Tests, tests, tests!
  Continuous integration
    Unit test of communication class SignalSlotable runs for all supported brokers
    Integration tests are repeated for JMS and most promising new broker
  Big test suit of our TestPortal for each release candidate and intermediate alpha releases
    Includes tests beyond Karabo framework (device packages)
    Integrated new stress tests
      high data rate
      message order

## Slide 11: Timeline of Refactoring
Autumn 2015: Worrying rate tests with message loss (data logging)
Nov. 2016: Karabo 2 released
  To commission the facility
Sept. 2017: First EuXFEL instruments go into production
2018: First serious studies of alternative brokers
  Mainly studies concerning MQTT protocol
April 2020: Official start of internal project to investigate broker protocols
  MQTT: Liked for IoT applications
  AMQP: Wall Street proven
Nov. 2020: Broker base class released in all APIs

## Slide 12: Timeline of Refactoring (ctd.)
May 2021: Experimental MQTT broker support
  Caveat: MQTT does not keep messages in order if sent from A to B via different routes
  Karabo operation requires order, but signals and direct slots cannot use the same route
    complicated and fragile custom code needed to keep order
Oct. 2021: Experimental AMQP and Redis broker support
  Message order integration test on CI
2022: Work on
  Robustness
  “Fail-over” for cases of lost broker connection

## Slide 13: Timeline of Deployment
March 2023: Deploy use of AMQP at first instrument SXP
  RabbitMQ broker provides ready-to-use monitoring
  Smooth start:
    Just like a normal Karabo deployment!
July 2023: Instrument with biggest control installation follows
Oct. 2023: Fix of a race condition in Karabo’s AMQP code
  Lead occasionally to crashes
Dec. 2023: Deploy AMQP facility wide (JMS @ EuXFEL is history!)
SXP, CTRL and DAQ staff March 2023

## Slide 14: Issues and Actions after Full AMQP Deployment
Jan. and April 2024: Crash of one RabbitMQ broker process (not Karabo)
  Fixed with hardware replacement and RabbitMQ upgrade
  “Fail-over” did not work
Spurious missing broker subscriptions
  If many subscriptions are run concurrently (e.g. if a data logger starts)
Repeated crashes when many devices in a single process start concurrently
 Spring 2024: Decision to rewrite the Karabo C++ interface to AMQP from scratch
  Incl. unit tests with concurrency situations
  Released June 2024
    Deployed for Karabo “backbone” and DAQ in July 2024
    “Fail-over” postponed to November release

## Slide 15: Issues and Actions after Full AMQP Deployment (ctd.)
Apr./Sept. 2024: AMQP Broker monitoring shows message queues for devices
  Identified as a CPU problem
    Overloaded host or Python (MDL) process
  No danger for communication in full installation (as the backlog of the JMS broker was)
    Each message queue on the broker has a limit
    Problem stays local

## Slide 16: Performance Reached
C++
  Single device on a server
    Withstands receiving small messages: 20 kHz
    Can send small messages at 17 kHz
  Server withstands simultaneous high sending and receiving rates
    Single receiver device 9.0-9.5 kHz
    20 kHz sending rate (latencies < 100 ms)
      200 senders at 100 Hz each
      1000 senders at 20 Hz
  Note: Much contingency
    Even GUI servers and data loggers receive less than 1 kHz
MDL (i.e. single threaded Python)
  Can send and receive in total ≥ 2 kHz
  Side effect: now pure Python broker client library  simplifies distribution

## Slide 17: Summary
Karabo control system communicates via a message broker
  Some deficiencies of the originally used JMS broker and OpenMQc client library spotted early
Replacing core technology in a used system is delicate
  Always need to be able to switch back
  Requires confidence in test coverage
  About five years from first serious studies to full AMQP deployment
    There are always short term goals that prevent more rapid progress
    Some things need to be iterated
The effort was worth it:
  No global danger for communication in a Karabo installation (less emergency call)
  Higher performance
  RabbitMQ broker ready for encryption