## Slide 1
This work is partly funded by the European Union’s Horizon 2020 Research and Innovation Programme under the Marie Sklodowska-Curie COFUND scheme with grant agreement No. 101034267.
Machine Learning for the Real-Time Analysis of X-ray Spectroscopic Data
Federico Zecchi, Marius Retegan, Pieter Glatzel
H2020 ENGAGE conference

## Slide 2: MOTIVATIONS FOR USING ML IN XAS DATA ANALYSIS
Synchrotron Datasets
Manual Analysis
Increasing Difficulty
Delays
Domain Expertise
Spectra Comparison
Time-Consuming
Large Datasets
Machine Learning
Maximize information
No Prior Knowledge Needed
Faster Analysis
ML Automation
Data Acquisition
Efficiency Boost
Beamline Operations

## Slide 3: OVERVIEW OF ML MODELS COMPLEXITY FOR SPECTROSCOPY DATA ANALYSIS
PCA
Typically used for data pre-processing, dimensionality reduction.
Tetef et al., Chem. Phys. Phys. Chem. 23, 23586 (2021).
Convolutional Neural Networks
Deep learning model for capturing spatial hierarchies. Often used in image analysis for feature extraction.
Mishra et al., Chemometrics and Intelligent Laboratory Systems 212, 104287 (2021).
Random Forest
Combines decisions from multiple predictors to improve accuracy.
Torrisi et al., npj Comput Mater 6, 109 (2020).

## Slide 4: DATASET AND MODEL TRAINING
Spectrum
calculation
Fe K-edge spectrum
Joly et al., J. Phys. Condens. Matter 21, 345501 (2009).
Coordination environment determination
Waroquiers et al., Acta Crystallogr B Struct Sci Cryst Eng Mater 76, 683-695 (2020).
Spectral
database
Random Forest Classifier
Training

## Slide 5: CALCULATED SPECTRA FOR OCTAHEDRAL AND TETRAHEDRAL ENVIRONMENTS
2689 spectra: 69% O:6, 31% T:4.

## Slide 6: CLASSIFICATION RESULTS ON TEST SET
Accuracy: 92.7±0.6%
Dataset was split in train (80% of data) and test (20% of data) sets.

## Slide 7: TEST SET PERTURBATION: NOISE
Metrics for different noise values
Photons counting statistic follows a Poisson distribution.
r: arrival rate; time interval; N: number of counts
Signal-to-noise ratio definition for shot noise:

## Slide 8: CLASSIFICATION OF EXPERIMENTAL DATA
Compound | CE | Full spectrum | Descriptors
α-FeOOH (Goethite) | O:6 | ✅ | ✅
ɣ-FeOOH (Lepidocrocite) | O:6 | ✅ | ✅
KFe3(SO4)2(OH)6 (Jarosite) | O:6 | ✅ | ✅
CuFeS2 (Chalcopyrite) | T:4 | ✅ | ✅
MgFe(SiO4) (Olivine) | O:6 | ✅ | ✅
FeN | T:4 | ✅ | ❌
FeO | O:6 | ✅ | ✅
FeS2 | O:6 | ✅ | ✅
FePO4 | T:4 | ❌ | ✅
Data collected at ID26 of ESRF

## Slide 9: SPECTRAL DESCRIPTORS
Dimensionality reduction improves model efficiency, reduces overfitting, and enhances interpretability.
Accuracy: 93.0±0.5%
Edge Position ()
Edge Slope ()
White Line Position ()
First Pit Energy ()
Guda et al., Npj Comput. Mater. 7, 203 (2021).

## Slide 10: SHAPLEY VALUES FOR MODEL INTERPRETATION
Complex ML models improve prediction accuracy but reduce interpretability.
SHAP values clarify feature importance by showing their impact on model predictions.
Waterfall plots illustrate how the prediction for a specific instance deviates from the average prediction across the entire dataset.
f(x): probability of classifying O:6 coordination.
O:6
T:4
arXiv:1705.07874

## Slide 11: COMPLETE DATASET: BEYOND BINARY CLASSIFICATION
1856 spectra (59%)
104 spectra (3%)
106 spectra (3%)
98 spectra (3%)
153 spectra (5%)
833 spectra (26%)

## Slide 12: SYNTHETIC MINORITY OVERSAMPLING TECHNIQUE
Chawla et al., J. Artif. Intell. Res. 16, 321–357, 2002.
Oversampling techniques are one way to solve class imbalances issues.

## Slide 13: SYNTHETIC MINORITY OVERSAMPLING TECHNIQUE
Oversampling techniques are one way to solve class imbalances issues.
SMOTE algorithm:
Randomly select a minority class sample.
Chawla et al., J. Artif. Intell. Res. 16, 321–357, 2002.

## Slide 14: SYNTHETIC MINORITY OVERSAMPLING TECHNIQUE
Oversampling techniques are one way to solve class imbalances issues.
SMOTE algorithm:
Randomly select a minority class sample.
Choose one sample among the k nearest neighbors, then compute the difference between the feature values.
Chawla et al., J. Artif. Intell. Res. 16, 321–357, 2002.

## Slide 15: SYNTHETIC MINORITY OVERSAMPLING TECHNIQUE
Oversampling techniques are one way to solve class imbalances issues.
SMOTE algorithm:
Randomly select a minority class sample.
Choose one sample among the k nearest neighbors, then compute the difference between the feature values.
Multiply the difference by a random number between [0,1], then add it to the chosen sample’s features.
Chawla et al., J. Artif. Intell. Res. 16, 321–357, 2002.

## Slide 16: SYNTHETIC MINORITY OVERSAMPLING TECHNIQUE
SMOTE

## Slide 17: MULTICLASSIFICATION
Only the training set is oversampled, the test set is fixed in size.
No oversampling - Accuracy = 70%
SMOTE - Accuracy = 79%
Class imbalances can be solved using oversampling techniques,
like Synthetic Minority Over-sampling Technique (SMOTE).
Chawla et al., J. Artif. Intell. Res. 16, 321–357 (2002).

## Slide 18: CONCLUSIONS
It is robust against shot noise, energy shifts, self-absorption.
In the case of severely underrepresented classes, oversampling techniques such as SMOTE can help improve the metrics of the model.
The Random Forest algorithm is reliable for classifying materials’ properties from calculated data.
Dimensionality reductions reduces overfitting, and enhances model interpretability.

## Slide 19
”Enabling the next generation of computational physicists and engineers”
This work is partly funded by the European Union’s Horizon 2020 Research and Innovation Programme under the Marie Sklodowska-Curie COFUND scheme with grant agreement No. 101034267.
Thank you for your attention!

## Slide 20: FDMNES vs EXPERIMENT