## Slide 1: 1st COLD Meeting: RF Activity Report
A. D’Elia

## Slide 2: Contents
Pulse Compression Studies:
  Benchmark with SLAC results;
  PSI-BOC pulse compressor studies;
Klystron needs
Layout update
Where we are

## Slide 3: Benchmark with SLAC results
Freq. (GHz) | 5.712 | W/O P.C.
Pin (MW) | 17.5 | 26.2***
Pulse length (s) | 2 | 1.65***
Pulse Compressor |  | 
 | 20 | -
Q0 | 200000 | -
Acc. Structure |  | 
 | 3.5 | 1
Q0 | 22500* | 20700*
Rsh** (Mohm/m) | 300 | 300
* In the original table I see 20700, SLAC confirmed they observe some variation from structure to structure, however final results do not change significantly.
** LINAC-Ohm (Rsh=V2/P), TTF included.
*** C-Band klystron, 50MW/1.5-2s are available (100Hz rep. rate).
NB: Pulse Compressor Output Power is sensitive to the speed of the phase ramp
SLAC
SLAC
SLAC
Pulse length=2s
Total Diss En=14.644 J
Phase ramp=180/50ns
1/3 less power with a Pulse Compressor
NB: SLAC does not consider a finite phase ramp

## Slide 4
Courtesy of R. Zennaro, PSI
34 C-Band BOC and 4 XBOC structures produced and operational: w/o any operational problem so far!!

## Slide 5: “Real” PSI-BOC parameters
(PSI-BOC)
Freq. (GHz) | 5.712
Pin (MW) | 35
Pulse length (s) | 2
BOC | 
 | 9.4
Q0 | 220000
Acc. Structure | 
 | 3.5
Q0 | 22500
Rsh (Mohm/m) | 300
A 35MW/2s klystron + PSI BOC works. NB: no margins, the final power from the klystron, should also include:
RF losses in the waveguide (~20%);
Always a 10% margin from Max power that the klystron can deliver.

## Slide 6: Studies with “real” PSI-BOC parameters
Freq. (GHz) | 5.712
Pin (MW) | 20-35
Pulse length (s) | 2-5
BOC | 
 | 9.4
Q0 | 220000
Acc. Structure | 
 | 1-3.5
Q0 | 22500
Rsh (Mohm/m) | 300
We are not considering any margin on the klystron input power.
Pin=35MW
Pulse length=2s
 structure variation
Pin =35MW
=2
Pulse length variation
Pulse length=4s
=2
Pklys variation

## Slide 7: Can we reduce the number of klystrons?
Freq. (GHz) | 5.712
Pin (MW) | 25
Pulse length (s) | 4
BOC | 
 | 9.4
Q0 | 220000
Acc. Structure | 
 | 2
Q0 | 22500
Rsh (Mohm/m) | 300
(PSI-BOC)
No Power reduction
No Power reduction
-30% in power applied at the output of the BOC
No Power reduction
We applied a 30% of power reduction at the output of the BOC to take into account WG losses and some klystron power margin.
Can we use a 50MW klystron, 4s pulse length to feed 2 cryomodules (4 x C3 structures)?

## Slide 8: Overall Layout
PINJ Entrance Door? 
load
GUN
Isolator
Vacuum Valve
IP
pen
valve
DC
35 MW
4.5ms, 4Hz
S-band*
load
Modulators SAT
WG switch
* EU S-Band=2.998GHz.
According to INFN: only 20-25MW/1.5ms needed.
Vacuum Valve
DC
?
load
C3 1m struct
C3 1m struct
DC
DC
Planar hybrid
50 MW
4 ms, 4-10Hz
C-band**
load
WG switch
Modulators SAT
BOC
DC
DC
Atten
Ph.
Shift.
C3 1m struct
?
Atten
** Only 25MW needed for COLD
Vacuum Valve
Vacuum Valve
WALL

## Slide 9: S-Band section
Outcome from last Injectors upgrade: New Linac Meeting (5th May 2025):
No issues to use a 35MW/4,5s to feed a GUN needing only <25MW/1,5s (PSI+SLAC+SCANDINOVA);
Better replacing RF windows with vacuum valves (SLAC);
Preliminary spec for RF loads correct: Max Power+~10% Margin (PSI);
To be addressed in the near future: what about temperature stability if “everything” outside the tunnel? (PSI+SLAC).
Outcome from last Meeting with SCANDINOVA (15th May 2025):
Isolator doesn’t exist in vacuum but only in SF6 To be asked to INFN-LNF who developed also a system using a BOC to reduce the power…
They can provide for integrated directional coupler in the klystron and reflected power interlock system;
They may provide for material for SAT if necessary;
They can offer guarantee extension of 1 year for ~5% on the final price;
They can help with LLRF (can suggest dedicated Companies/Institutes) if necessary.
load
GUN
Isolator
Vacuum Valve?
IP
pen
valve
DC
35 MW
4.5ms, 4Hz
S-band*
load
Modulators SAT
WG switch
* EU S-Band=2.998GHz.
According to INFN: only 20-25MW/1.5ms needed.
Vacuum Valve or RF Window?
DC
?
RF Window?

## Slide 10: C-Band Section
Outcome from last Injectors upgrade: New Linac Meeting (5th May 2025):
No issues to use a 50MW/4s for COLD (PSI+SLAC+SCANDINOVA);
Better replacing RF windows with vacuum valves (SLAC);
Preliminary spec for RF loads correct: for COLD we calculate 50MW Max reflected power from the 2 structures  2 identical RF loads for SAT and Ref. Power (50MW+10% Margin) (PSI);
PSI has C-Band switches and can suggest a Company which can provide for;
To be addressed in the near future: what about temperature stability if “everything” outside the tunnel? (PSI+SLAC)
Outcome from last Meeting with SCANDINOVA (15th May 2025):
They can provide for integrated directional coupler in the klystron and reflected power interlock system;
What about the required flatness for the full 4s pulse? They can provide +/-1.5%. However using a pulse compressor this should not be a problem. Of course tbc.
They may provide for material for SAT if necessary;
They can offer guarantee extension of 1 year for ~5% on the final price;
They can help with LLRF (can suggest dedicated Companies/Institutes) if necessary.

## Slide 11: Market survey: preliminary outcome
C-Band: 5.712GHz – All Under Vacuum |  |  | 
Components | Company | Price | Spec
Waveguides |  |  | 
Straight | MEGA, TSC |  | 60MW peak, 4s, Rep. Rate=10Hz
Elbow | MEGA, TSC |  | 60MW peak, 4s, Rep. Rate=10Hz
Switch | NIHON KOSHUA (tbc with PSI) |  | 60MW peak, 4s, Rep. Rate=10Hz
Load | ? (However same as PSI) |  | 60MW peak, 4s, Rep. Rate=10Hz
Planar Hybrid | NIHON KOSHUA (tbc with PSI) |  | 140MW (?) peak, 4s, Rep. Rate=10Hz
Directional Couplers | TSC (probably), MEGA (?) |  | -
EU S-Band: 2.998GHz – All Under Vacuum |  |  | 
Components | Company | Price | Spec
Waveguides |  |  | 
Straight | MEGA, TSC, SPINNER |  | 40MW peak, 4.5s, Rep. Rate=10Hz
Elbow | MEGA, TSC, SPINNER |  | 40MW peak, 4.5s, Rep. Rate=10Hz
Switch | ? |  | 40MW peak, 4.5s, Rep. Rate=10Hz
Load | ? (However same as INFN) |  | 40MW peak, 4.5s, Rep. Rate=10Hz
Isolator | SPINNER? (However same as INFN) |  | 40MW peak, 4.5s, Rep. Rate=10Hz
Directional Couplers | MEGA, TSC, SPINNER |  | -
TSC suggested DESY Type Flanges
I contacted MEGA, TSC and SPINNER for a preliminary survey for rough estimation of the prices and, more important to identify who can provide for what. Here below the first outcome.
Last minute addition from Pawel: we need to consider also arc detector system

## Slide 12: Overall Layout 2
In case the planar Hybrid can’t manage BOC Peak Power output
load
C3 1m struct
C3 1m struct
50 MW
4 ms, 4-10Hz
C-band**
load
WG switch
Modulators SAT
DC
DC
Atten
Ph.
Shift.
C3 1m struct
?
Atten
** Only 25MW needed for COLD
Vacuum Valve
Vacuum Valve
Planar hybrid
BOC
BOC
load
GUN
Isolator
Vacuum Valve?
IP
pen
valve
DC
35 MW
4.5ms, 4Hz
S-band*
load
Modulators SAT
WG switch
* EU S-Band=2.998GHz.
According to INFN: only 20-25MW/1.5ms needed.
Vacuum Valve or RF Window?
?
RF Window?
WALL

## Slide 13: Services
ELEC:
S-Band
1 klystron+Modulator: same as for LINAC Refurbishment
C-Band
1 klystron+Modulator: SCANDINOVA will send us an estimation
CEM (grounding): needs to be separated? What about separation w.r.t. present LINAC?
Laser? Asked FRASCATI??
Magnets?
Water Cooling:
Klystron and Modulators:
  S-Band: same as for LINAC Refurbishment (flow rate~120 l/min?);
  C-Band:
    According to PSI, considering their system working at 50MW/3s/100Hz (15kW)  100l/min per channel; for 50MW/4s/10Hz (2kW)  15l/min;
    According to SCANDINOVA, CANON always asks the klystron working at the nominal flow for the highest possible nominal power  ~100l/min per channel (klystron will be basically the same as PSI): SCANDINOVA will send us an estimation;
Gun: asked FRASCATI??
BOC: from PSI “[Each BOC] needs a dedicate heater and a dedicate variable valve, both are controlled by a feedback loop which stabilize the BOC temperature to 0.002 °C rms. Probably you do not need the same stability (for a test stand 0.1°C is enough) but you still need to have the possibility to warm up the cooling water. Our cooling water temperature range is 35 +- 7 °C. I suggest to use a commercial device for cooling/heating (for some installations with moderate water flow and where we do not need stability we use products from Regloplas at PSI) with this solution you do not need a variable valve.”
LOADS: to be asked to PSI/FRASCATI/SLAC;
For specific WG’s: Hybrid and Directional Couplers (for thermal stability*). Isolator?
LASER? Asked FRASCATI?
Magnets?
* Needs temperature control loop?