## Slide 1: 2nd COLD Meeting: RF Activity Report
A. D’Elia

## Slide 2: Preliminary Layout
* EU S-Band=2.998GHz.
According to INFN: only 20-25MW/1.5ms needed.
load
C3 1m struct
C3 1m struct
50 MW
4 ms, 4-10Hz
C-band**
load
WG switch
Modulators SAT
DC
DC
Atten
Ph.
Shift.
C3 1m struct
Atten
** Only 25MW needed for COLD
Vacuum Valve
Vacuum Valve
Planar hybrid
BOC
BOC
load
GUN
Isolator under SF6
IP
pen
valve
DC
35 MW
4.5ms, 4Hz
S-band*
load
Modulators SAT
WG switch?
Vacuum?
RF Window
RF Window?
WG Switches not mandatory
WALL

## Slide 3: Market survey: preliminary outcome
C-Band: 5.712GHz – All Under Vacuum |  |  | 
Components | Company | Price | Spec
Waveguides |  |  | 
Straight | MEGA, TSC |  | 60MW peak, 4s, Rep. Rate=10Hz
Elbow | MEGA, TSC |  | 60MW peak, 4s, Rep. Rate=10Hz
Switch | NIHON KOSHUA (tbc with PSI), but needed? |  | 60MW peak, 4s, Rep. Rate=10Hz
Load | ? (However same as PSI) |  | 60MW peak, 4s, Rep. Rate=10Hz
Planar Hybrid | NIHON KOSHUA (tbc with PSI) |  | 140MW (?) peak, 4s, Rep. Rate=10Hz
Directional Couplers | TSC (probably), MEGA (?) |  | -
EU S-Band: 2.998GHz – All Under Vacuum |  |  | 
Components | Company | Price | Spec
Waveguides |  |  | 
Straight | MEGA, TSC, SPINNER |  | 40MW peak, 4.5s, Rep. Rate=10Hz
Elbow | MEGA, TSC, SPINNER |  | 40MW peak, 4.5s, Rep. Rate=10Hz
Switch | Needed? |  | 40MW peak, 4.5s, Rep. Rate=10Hz
Load | ? (However same as INFN) |  | 40MW peak, 4.5s, Rep. Rate=10Hz
Isolator | SPINNER? (However same as INFN) |  | 40MW peak, 4.5s, Rep. Rate=10Hz – SF6
Directional Couplers | MEGA, TSC, SPINNER |  | -
NEW: RF Window | SPINNER can provide, MEGA and TSC not contacted yet |  | 
TSC suggested DESY Type Flanges
I contacted MEGA, TSC and SPINNER for a preliminary survey for rough estimation of the prices and, more important to identify who can provide for what. Here below the first outcome.
Addition from Pawel: we need to consider also arc detection system

## Slide 4: Services
ELEC:
S-Band
1 klystron+Modulator: 35MW x 6s (max) x 10Hz (that should be the same as for LINAC Refurbishment)
C-Band
1 klystron+Modulator: 50MW x 4s (nominal, max?) x 10Hz
CEM (grounding): needs to be separated? What about separation w.r.t. present LINAC?
Laser? Asked FRASCATI??
Magnets?
Water Cooling:
Klystron and Modulators:
  S-Band from SCANDINOVA: 60-65 l/min x klystron + 10 l/min x solenoid (that should be the same as for LINAC Refurbishment);
  C-Band from SCANDINOVA: 70-80 l/min x klystron + 11 l/min x solenoid ;
Gun: 100-200W to be dissipated with high temperature stability <0.1°C (Frascati use a dedicated chiller system);
BOC: from PSI “[Each BOC] needs a dedicate heater and a dedicate variable valve, both are controlled by a feedback loop which stabilize the BOC temperature to 0.002 °C rms. Probably you do not need the same stability (for a test stand 0.1°C is enough) but you still need to have the possibility to warm up the cooling water. Our cooling water temperature range is 35 +- 7 °C. I suggest to use a commercial device for cooling/heating (for some installations with moderate water flow and where we do not need stability we use products from Regloplas at PSI) with this solution you do not need a variable valve.”
LOADS:
  S-Band ISOLATOR: 100-200W to be dissipated, temperature stability of about 1°C;
  C-Band: ??;
For specific WG’s: Hybrid and Directional Couplers (for thermal stability*). Isolator? To be asked to SPINNER, apparently the only one, so far, able to provide for such a component.
LASER? Asked FRASCATI?
Magnets?
* Needs temperature control loop?

## Slide 5: Ongoing CFT(s)
So far we started the procedure to procure the S-BAND RF Unit for the GUN: not possible to go for a direct contract although same specifications of LINAC Refurbishment Unit (CFT done at the end of last year).
Main Objectives:
Purchase same RF Unit such as the one for the LINAC Refurbishment (w/o C-Band Option);
Purchase on the COLD Budget of this year 2025;
FAT in 9-12 months with Option of delaying SAT until LINAC Refurbishment Activity is over (max June 2027).
Status:
Created a Commercial Consultation for CFT-3572;
Writing technical specification: small modification of those for CFT-3461 (thanks a lot to Marc and Mathieu for the specs!!!);
According to David Flood this is the scheduling to realistically place the order for the end of the year (November 2025?):
  Mid-July: dispatch to the supplier;
  Mid-July (at the latest): Technical specification + PBPF (Price Breakdown Pro-Forma);
  End of August: end date for supplier to answer;
  End of August: evaluation grid.