## Slide 1: ISDD DAY – MEG CHALLENGES
- Machine Projects Portfolio and technical challenges
- Beamline Projects Portfolio and technical challenges
- Staff challenges and conclusion
MEG Challenges — Presentation Outline

## Slide 2: Machine Projects Portfolio and technical challenges
EBS machine
ASD projects
IDM projects
New generation of revolver
in vacuum undulator
Short period/magnetic compensation
Challenges = dimensions/new design
Courtesy B. Ogier
HTS source for BM18
Challenges : T=65K/HTS coil in vacuum design
Booster upgrade
Challenges : manufacture follow up and installation of 18 quadrupoles

## Slide 3: Machine Projects Portfolio and technical CHALLENGES challenges
EBS machine
ASD projects
IDM projects
New generation of revolver
in vacuum undulator
HTS source for BM18
Booster upgrade
Injection upgrade

## Slide 4: Machine Projects Portfolio and technical CHALLENGES
Fully transparent off-axis injection is possible using non-linear kicker (NLK) injection:
Operating at MAXIV and SIRIUS: demonstrated method
Zero field and gradient seen by stored beam
Requires a full re-design of injection straight and end of TL2
NLK design and maintaining high efficiency challenging
Challenges = full re-design of injection and end of TL2 + NLK design
Courtesy = T. Brochard
D. Baboulin/T. Brochard

## Slide 5: Machine Projects Portfolio and technical CHALLENGES challenges
EBS machine
ASD projects
IDM projects
New generation of revolver
in vacuum undulator
HTS source for BM18
Booster upgrade
Injection upgrade
COLD project

## Slide 6: Machine Projects Portfolio and technical CHALLENGES
C2 cold copper
Operation
Linac
Demonstrator
COLD
A demonstrator to prove
high gradient cryogenic accelerating structures
for users facility grade operation
at low repetition rate.
The pre-injector of a new 6GeV linac.
Challenges = collect 3D model of components from SLAC/INFN –
Participate to the design of missing parts
Integrate them in the existing building while maintaining current linac operations (maintenance)
=> Provide the necessary data and inputs to perform radiation calculations for ASNR validation
Courtesy = S. Liuzzo et al.

## Slide 7: Machine Projects Portfolio and technical CHALLENGEShallenges
EBS machine
ASD projects
IDM projects
New generation of revolver
in vacuum undulator
HTS source for BM18
Booster upgrade
Injection upgrade
COLD project
= Linac upgrade
FE UPGRADE

## Slide 8: FE UPGRADE
=> More power on FE components (slits, shutter)
Insertion device
(length)
Gap
(mm)
Total Power
(kW)
Power Density (in
16.1m)
(W/mm2)
Comment
CPMU16.4 (2m)
5.0 mm
12.9
1545
Installed and used on ID03
CPMU16.4 (2m)
4.0 mm
20.1
1947
ID03
-
4mm (“mini
-
beta”)
CPMU20.5 (4m)
5.5 mm
29.6
2716
Plan for double CPMU ID20/ID14
Courtesy P. Brumund

## Slide 9: BEAMLINE Projects Portfolio and technical CHALLENGEShallenges
BEAMLINES
ID11 - TDR
Challenges manage beam power = Source = 2*CPMU – 18 and 20,5 using the entire beam > 2KW
=> Precise knowledge of power beam from the source to the sample, as well as the limits of each equipment
=> Re-design safety component such as photon absorber and use watch dog for other components
Courtesy = Joachim Leonardon

## Slide 10: BEAMLINE Projects Portfolio and technical CHALLENGEShallenges
BEAMLINES
ID11 - TDR
ID18 - TDR

## Slide 11: BEAMLINE Projects Portfolio and technical CHALLENGES - ID18hallenges
Challenges = probably not related to the heat load and optical equipment, but rather to the nano end stations design
KB focalization
25 nm beam sizes
Sample holder
Courtesy F. villar
ID16A  ID18 end station specifications
 | ID16A | ID18
Scanning range | 50 µm | 1 mm
Speed | 5 µm/s | 500 µm/s
volume | 10-5 mm3 | 10 mm3
Resolution | 10 nm | 10 nm
=> Real-time controller is necessary
Dynamic modeling is crucial (eg Simulink) to assist design
Determination of transfer function
Evaluation of perturbation effect (vibration …)
Evaluation of final performance
Increased bandwidth will require new actuators
voice coil and direct drive, maglev actuator ?
higher servo bandwidth + higher disturbance rejection and better tracking performance

## Slide 12: BEAMLINE Projects Portfolio and technical CHALLENGEShallenges
BEAMLINES
ID11 - TDR
ID18 - TDR
ID10 - COH

## Slide 13: BEAMLINE Projects Portfolio and technical CHALLENGEShallenges
WAXS
4 Detectors @ 3m
From 5 to 45º
SAXS
2 detectors from 3 to 7m
From 0 to 5º
END STATION
- Ovens/peltier
Sample of few Kg
µm resolution
- Ptychography
10mm membranes
20nm resolution
OPTICAL COMPONENTS
MEG engineering : 80 days
MEG Drafting : 40 days
MEG PAMU : 30 days
Ressources in 2025
Courtesy = Carole Clavel
    Technical challenges :
    Extractable vacuum tube for SAXS detector
    WAXS detectors positioning (@3m on a large angular range)
    WAXS very large vacuum chamber
    Ptychography end-station (20nm resolution & sample position measurement)
    Windowless and in-vacuum from source to sample
    Total budget ~1.5M €

## Slide 14: BEAMLINE Projects Portfolio and technical CHALLENGEShallenges
BEAMLINES
ID11 - TDR
ID18 - TDR
ID10 - COH
DCMs

## Slide 15: BEAMLINE Projects Portfolio and technical CHALLENGEShallenges
Technical challenges =
Operation and maintenance (3*DCMs)
production (2*DCMs)
study of a non standard for ID20(1*DCM)
Procurement of high quality components
Development of new actuators / voice coil

## Slide 16: STAFF CHALLENGES and CONCLUSION
1 – Many technical challenges are good for maintaining motivation and improving staff skills
2 - The current workload is not aligned with MEG team’s capacity

## Slide 17: STAFF CHALLENGES and CONCLUSIONS
EBS upgrade
3 COD
5

## Slide 18: STAFF CHALLENGES and CONCLUSION
1 – Many technical challenges are good for maintaining motivation and improving staff skills
2 - The current workload is not aligned with MEG team’s capacity
Impact on our medium-term development capacity
Impact on staff motivation
3 - This year we identify critical skills and obtain one position for a calculation engineer, one position in anticipation of retirement for beam transport modelling engineer and for a measurement technician for mechatronic system.
- Recruitment of one PhD student to help with dynamic modeling and Maglev actuator development (ID18 nano tomo end-station).

## Slide 19: ISDD DAY – MEG CHALLENGES
Thank you for your attention

## Slide 20
Jira project 2025 = 1500 days
Jira project 2026 = 2000 days
MEG capacity = 1900 days