## Slide 1: SOLEIL Insertion Devices and Prospects for the Upgrade
O. Marcouillé on behalf of SOLEIL II Project Team
Insertion Device Workshop 2026, 15 – 16 May 2026 - Deauville

## Slide 2: Contents
SOLEIL Synchrotron
Insertion Devices at SOLEIL
From SOLEIL to SOLEIL II
Three new Insertion Devices for SOLEIL II
Re-use of Insertion Devices for SOLEIL II

## Slide 3: Technical and scientific environment: SOLEIL Synchrotron
Photon energy
Synchrotron SOLEIL
Energy: 2.75 GeV
Current: 500 mA
Emittance: 3.9 nm.rad
Coupling: 1%
Energy spread: 0.125 %
IDs
24h/24h and 7j/7j
THz  Hard X-Rays:
9 BM based beamlines
20 ID based beamlines
  8 Short Straight Section
  8 Medium Straight Section
  4 Long Straight Section

## Slide 4: Insertion Devices at SOLEIL
 | SOLEIL | 
 | Straight Section | Insertion Device
LUCIA | SDM16 | HU52
PSICHE | SDC03 | IVW50
PLEIADES | SDM04 | HU80 - HU256
DEIMOS | SDM07 | HU52 - EMPHU65
PUMA | SDM06 | W164
CRISTAL | SDC06 | CPMU18
GALAXIES | SDC07 | IVU20
TEMPO | SDM08 | HU80 - HU44
DESIRS | SDL05 | HU640
HERMES | SDM10 | HU64 - HU42
PXI | SDC10 | IVU20
PXII | SDM11 | IVU24
SWING | SDC11 | IVU20
ANTARES | SDM12 | HU60 - HU256
ANATOMIX | SDL13 | CPMU18
NANOSCOPIUM | SDL13 | CPMU18
SEXTANTS | SDM14 | HU80 - HU44
SIXS | SDC14 | IVU20
SIRIUS | SDC15 | HU36
CASSIOPEE | SDM15 | HU60 - HU256
Number | Technology | Type | Magnetic period (mm) | Length (m) | Type of polarization | Prefix
1 | Electromag. | Undulator | 640 | 10 | all | HU
3 | Electromag. | Undulator | 256 | 3.54 | LH/LV/Circ | HU
1 | Electro-PPM | Undulator | 65 | 1.8 | LH/LV/Circ | EMPHU
12 | APPLE II | Undulator | 36 to 80 | 1.8 | LH/LV/LT/Circ | HU
1 | Out-vacuum | Wiggler | 164 | 3.2 | LH | W
5 | In-vacuum | Undulator | 20 and 24 | 2 | LH | IVU
1 | In-vacuum | Wiggler | 50 | 2 | LH | IVW
3 | Cryogenic | Undulator | 18 | 2 | LH | CPMU
One of Long Straight Section accommodates large undulator period
One of Long Straight Section accommodates canted undulators

## Slide 5: Insertion Device at SOLEIL: Polarized Insertion Devices
1.8 m
1.8 m
6.6 m
 | SOLEIL | 
 | Straight Section | Insertion Device
LUCIA | SDM16 | HU52
PSICHE | SDC03 | IVW50
PLEIADES | SDM04 | HU80 - HU256
DEIMOS | SDM07 | HU52 - EMPHU65
PUMA | SDM06 | W164
CRISTAL | SDC06 | CPMU18
GALAXIES | SDC07 | IVU20
TEMPO | SDM08 | HU80 - HU44
DESIRS | SDL05 | HU640
HERMES | SDM10 | HU64 - HU42
PXI | SDC10 | IVU20
PXII | SDM11 | IVU24
SWING | SDC11 | IVU20
ANTARES | SDM12 | HU60 - HU256
ANATOMIX | SDL13 | CPMU18
NANOSCOPIUM | SDL13 | CPMU18
SEXTANTS | SDM14 | HU80 - HU44
SIXS | SDC14 | IVU20
SIRIUS | SDC15 | HU36
CASSIOPEE | SDM15 | HU60 - HU256
Medium Straight Section  Up to 2 insertion devices

## Slide 6: Insertion Device at SOLEIL
HU640
HU256
IVW50
IVU
CPMU18
W164
APPLE II

## Slide 7: From SOLEIL to SOLEIL II: Straight Section length
SOLEIL II
Objective:
Increase of the Brightness
(2 orders of magnitude)
Decrease of the horizontal emittance
from 3.9 nm.rad to 85 pm.rad
Strong Increase of the number of guiding equipments (Dipoles, Qpoles, Spoles …)
Straight Section | SOLEIL | SOLEIL II | Unit
Long | 11.6 | 8 | m
Medium | 6.6 | 4.26/3.8 | m
Short | 3.6 | 3.1 | m
TOTAL | 128 | 90 | m
Ratio to circumference | ~40 | ~25 | %
Spectral domain
SOLEIL II lattice
SOLEIL lattice

## Slide 8: From SOLEIL to SOLEIL II: ID Phase1 (P1)
 | SOLEIL |  | SOLEIL II | 
 | Straight Section | Insertion Device | Straight Section | Insertion Device P1
LUCIA | SDM16 | HU52 | SD03C | IVU24
PSICHE | SDC03 | IVW50 | SD04C | IVW50
PLEIADES | SDM04 | HU80 - HU256 | SD05MC | HU60
DEIMOS | SDM07 | HU52 - EMPHU65 | SD06L | DUAL HU52 - EMPHU65
PUMA | SDM06 | W164 | SD07MC | IVU20
CRISTAL | SDC06 | CPMU18 | SD08C | CPMU18
GALAXIES | SDC07 | IVU20 | SD09C | IVU20
TEMPO | SDM08 | HU80 - HU44 | SD10ML | DUAL HU44 - HU80
DESIRS | SDL05 | HU640 | SD11L | APU250
HERMES | SDM10 | HU64 - HU42 | SD12ML | DUAL HU42 - HU64
PX-ID | SDC10 | IVU20 - IVU24 | SD13C | IVU20
SWING | SDC11 | IVU20 | SD14C | IVU20
ANTARES | SDM12 | HU60 - HU256 | SD15MC | HU80
ANATOMIX | SDL13 | CPMU18 | SD16L | CPMU18
NANOSCOPIUM | SDL13 | CPMU18 | SD16L | CPMU18
SEXTANTS | SDM14 | HU80 - HU44 | SD17MC | AX42
SIXS | SDC14 | IVU20 | SD18C | IVU20
SIRIUS | SDC15 | HU36 | SD19C | HU36
CASSIOPEE | SDM15 | HU60 - HU256 | SD20ML | DUAL HU44 - HU130
 |  |  |  | 3 New Insertion Devices
 |  |  |  | Start of SOLEIL II: mid2030
 | underline = | To be re-installed | bold = | To be constructed
3 new insertion devices
All BL start with synchrotron radiation
  Some BL:with only 1 ID
  Some BL start with 2 IDs
Re-use of the majority of existing IDs:
  Polarized IDs: DUAL solution
  IVU-IVW-CPMU
    Gap: 5.5 mm 4.5 mm
    Minor mechanical changes
Phase 1: Start of SOLEIL II

## Slide 9: From SOLEIL to SOLEIL II: ID Phase1 (P1) and Phase 2 (P2)
 | SOLEIL |  | SOLEIL II |  | 
 | Straight Section | Insertion Device | Straight Section | Insertion Device P1 | Insertion Device P2
LUCIA | SDM16 | HU52 | SD03C | IVU24 | IVU24
PSICHE | SDC03 | IVW50 | SD04C | IVW50 | CPMW
PLEIADES | SDM04 | HU80 - HU256 | SD05MC | HU60 | AX63
DEIMOS | SDM07 | HU52 - EMPHU65 | SD06L | DUAL HU52 - EMPHU65 | DUAL HU52 - EMPHU65
PUMA | SDM06 | W164 | SD07MC | IVU20 | CPMU*
CRISTAL | SDC06 | CPMU18 | SD08C | CPMU18 | CPMU18
GALAXIES | SDC07 | IVU20 | SD09C | IVU20 | CPMU*
TEMPO | SDM08 | HU80 - HU44 | SD10ML | DUAL HU44 - HU80 | DUAL HU40-HU70
DESIRS | SDL05 | HU640 | SD11L | APU250 | APU250
HERMES | SDM10 | HU64 - HU42 | SD12ML | DUAL HU42 - HU64 | DUAL HU42 - HU64
PX-ID | SDC10 | IVU20 - IVU24 | SD13C | IVU20 | CPMU*
SWING | SDC11 | IVU20 | SD14C | IVU20 | CPMU*
ANTARES | SDM12 | HU60 - HU256 | SD15MC | HU80 | DUAL HU60 – HU90
ANATOMIX | SDL13 | CPMU18 | SD16L | CPMU18 | CPMU18
NANOSCOPIUM | SDL13 | CPMU18 | SD16L | CPMU18 | CPMU18
SEXTANTS | SDM14 | HU80 - HU44 | SD17MC | AX42 | CPMUE38
SIXS | SDC14 | IVU20 | SD18C | IVU20 | CPMU*
SIRIUS | SDC15 | HU36 | SD19C | HU36 | AX38
CASSIOPEE | SDM15 | HU60 - HU256 | SD20ML | DUAL HU44 - HU130 | DUAL HU44 - HU130
 | underline = | To be re-installed | bold = | To be constructed | 
Phase 2: towards full Perf.
All existing IDs will be
progressively replaced
CPMU: Period to be optimized

## Slide 10: Re-use of existing polarized undulators: DUAL solution
Undulators for DEIMOS Beamline
Undulators of HERMES Beamline
Undulators of TEMPO beamline

## Slide 11: Implementation on Medium Straight Section
SOLEIL
1.8 m
1.8 m
6.6 m
SOLEIL II
3.8/4.26 m
Undulator
« single »
DUAL Undulator

## Slide 12: DUAL undulators
Parking mode
Operation mode
Development of plateform:
  For existing ID
  For new ID in a next step
Reproducibility of transverse re-positionning:
  Horizontal: 10 µm
  Vertical: 6 µm
Ground vibrations during motorized switch bw IDs
  Longitudinal: 200 nm
  Vertical: 40 nm
Motorized DUAL Plateform
2.5 m
In memory of Fabien …

## Slide 13: ID positionning
F. Briquez, M. Sebdaoui / SOLEIL
REPRODUCIBILITY AND STABILITY DURING 96 HOURS
Excursion (µm)
33 CYCLES OF 1H00
NO CYCLE
F. Briquez, F. Blache, M. Sebdaoui, B. Luluan
50 CYCLES OF 1H00
NO CYCLE

## Slide 14: Vibrations during ID Switch
Accelerometers
Frequency (Hz) | Vertical displacement (µm)
277 | 0,170
407 | 0,082
43 | 0,139
228 | 0,026
91 | 0,031
173 | 0,016
133 | 0,020
84 | 0,030
Fréquence (Hz) | Longitudinal displacement (µm)
285 | 0,036
352 | 0,015
375 | 0,011
202 | 0,015
228 | 0,013
251 | 0,011
152 | 0,018
401 | 0,006
135 | 0,010
142 | 0,008
42 | 0,024
88 | 0,007
Z. Fan

## Slide 15: Three New Insertion Devices
APU250 for DESIRS beamline
DUAL HU130-HU44 for CASSIOPEE beamline
APPLE X for SEXTANTS beamline

## Slide 16: APU250* for DESIRS II Beamline : Phase dependant operation
Parameters | Values | Unit
Period number | 20 | -
Magnetic period | 250 | mm
Permanent magnets | NdFeB | -
Magnetization | 1.37 | T
Max. magnetic field | 0.46 | T
Spectral Domain | 5 - 40 | eV
Polarisation modes | All | -
Magnetic force reduction
Main system
11 mm
11 mm
25 mm
*: Carr. (1992). Design study for an adjustable phase undulator. Review of Scientific Instruments, 347-351.
Photon energy and polarization state changed
With dephasing of magnet arrays
Counterforce magnet: force reduction  4 to 8

## Slide 17: APU250 for DESIRS II Beamline: Mechanical design
Prototype of magnets support wire-machined at SOLEIL
150 magnets in fabrication for 3-period prototype using
  « Conventional » magnets by MAGSOUND (Ningbo, CHINA)
  Recycled magnets by MagREEsource (Grenoble, FRANCE)
  Sophie Rivoirard from MAGREESource will give more details in a dedicated talk
   Check magnetic field, demagnetization and local deformation
S. Bonnin
A. Mary / A. Berlioux
5 m

## Slide 18: APU250 for DESIRS II Beamline: First Recycled Magnets
Sample | Matière APU250
Date | 24/03/2026
Temperature (°C) | 21,3
Applied magnetic field (T) | 5,0
Volume (mm3) | 1582
Shape | disk
N | 0,44
Q_dBtail | 3,8
Density | 7,50
Br (T) | 1,375
Mmax (T) | 1,449
HcB (kA/m) | 1047
HcJ (kA/m) | 1225
(BH)max (kJ/m3) | 364
(BH)max (MGOe) | 45,7
SQknee | 0,94
Grade | N45M
Counterforce Magnets
Main Magnets
MagREESource
Zn coating

## Slide 19: APU250 for DESIRS II Beamline: First Recycled Magnets
Counterforce magnet
Main magnet
Magnetization angle < 1°
M
Alpha
Beta
MagREESource

## Slide 20: DUAL HU130-HU44 for CASSIOPEE II Beamline
HU130
Gx = 14 mm
Gz = 14 mm
M. Valléau
HU44
Gz = 12.5 mm
Parameters | HU130 | HU44 | Unit
Type | APPLE I | APPLE II | -
Period number | 15 | 45 | -
Magnetic period | 130 | 44 | mm
Permanent magnets | NdFeB | NdFeB | -
Magnetization | 1.32 | 1.32 | T
Max. magnetic field | 0,873 | 0.87 | T
Spectral Domain | 10 - 300 | 300 - 1500 | eV
Polarisation modes | LH/LV/LT/Circ | LH/LV/LT/Circ | -
APPLE I
APPLE II
A. Lejollec
DUAL

## Slide 21: AX42 for SEXTANTS II Beamline
M. Valléau
Parameters | Values | Unit
Period number | 47 | -
Magnetic period | 42 | mm
Permanent magnets | NdFeB | -
Magnetization | 1.37 | T
Max. magnetic field | 1,156 | T
Spectral Domain | 150 - 1800 | eV
Polarisation modes | LH/LV/LT/Circ | -

## Slide 22: IVU-CPMU at SOLEIL II
Technical changes
Towards shorter periods: CPMU12
Robotics developments

## Slide 23: IMPLEMENTATION IN SHORT STRAIGHT SECTION
SOLEIL
SOLEIL II
IVU/CPMU
IVU/CPMU
2.378 m
3.1 m
3.6 m
Main issue
Space
Mechanical connexion

## Slide 24: IVU/IVW/CPMU: TECHNICAL CHANGES
Storage Ring-IVU interface to be changed
Shorter ID correctors
Shorter valve
Compact system: BPM/bellows/ID correctors
ID CORRECTOR | LENGTH (mm) | MAGNETIC FORCE (G.m) | MAGNETIC GAP (mm)
EXISTING | 100 | 5 | 100
UPGRADE | 50 | 5 | 50
K. Tavakoli

## Slide 25: Short period CPMU: CPMU12
Change of technical approach Prototype: 1m long CPMU12 with 12 mm period in the frame of LEAPS INNOV
More details in Mathieu Valléau talk
Less time consumption
To install magnets
M. Valléau / P. Berteaud / R. Baillier / S. Pautard / A. Berlioux / S. Bonnin
Single support
Cu Super-module
8-periods
S. Steel Super-module

## Slide 26: Robotics development
Objective: Automatization of repetitive tasks
Initial developments in 3 steps:
  Individual measurement of single modules
  Mounting of modules on girders
  Magnetic Corrections
Development for SuperModules
L. Hernandez
M. Valleau
F. Briquez
Single module measurements
26
Mechanical reference
3 laser arms
L. Hernandez, M. Valléau
L. Hernandez, M. Valléau
SuperModule measurement and tuning
Hall probe
More details in Mathieu Valléau talk
Magnet/Pole position
Magnet/Pole correction
Supermodule measurement

## Slide 27: Conclusion
Overview of present insertion devices of SOLEIL
Three new insertion devices at the start of SOLEIL II
Re-use of IVU-IVW-CPMUs
Re-use of EPUs
Developments for SOLEIL II

## Slide 28: Acknowledgements
Magnetism and Insertion Group
M.-E. Couprie, M. Valléau, P. Berteaud, F. Blache, R. Baillier, A. Esper, S. M. Khan, C. Kitégi, F. Marteau, T. Mutin, C. Tournier, J. Vétéran
Mechanical Engineering Group
S. Bonnin, A. Berlioux, A. Mary, S. Pautard, K. Tavakoli, Z. Fan
Electronic Group
L. Hernandez
Accelerators Physics Group
P. Brunelle, L. S. Nadolski
Beamline Scientists
F. Bertrand, P. Fertey, L. Nahon, N. Jaouen
THANK YOU FOR YOUR ATTENTION