## Slide 1: CASPER
Alexandre Arsenault and Marco Calvi
ID workshop, May 15, 2026
Compact Arbitrary Superconducting Polarization Emitting Radiator
Notes: Mention that CASPER is also a measurement facility

## Slide 2: Compact Arbitrary Superconducting Polarization Emitting Radiator
SwissFELplus upgrade requiring high field and variable polarization:
  Aramis afterburn
  New Porthos beamline

## Slide 3: Compact Arbitrary Superconducting Polarization Emitting Radiator
Y. Ivanyushenkov, Proceedings of the 5th Int. Particle Accelerator Conf., vol. IPAC2014, p. 3 pages, 2014
Universal superconducting undulator
Concentric helical undulators
Inner helix -> Right-handed
Outer helix -> Left-handed

## Slide 4: Compact Arbitrary Superconducting Polarization Emitting Radiator
CASPER undulator: Intertwined helices
Layer 1

## Slide 5: Compact Arbitrary Superconducting Polarization Emitting Radiator
CASPER undulator: Intertwined helices
Layer 2

## Slide 6: Compact Arbitrary Superconducting Polarization Emitting Radiator
CASPER undulator: Intertwined helices
Layer 3

## Slide 7: Compact Arbitrary Superconducting Polarization Emitting Radiator
CASPER undulator: Intertwined helices
Layer 4

## Slide 8: Compact Arbitrary Superconducting Polarization Emitting Radiator
CASPER undulator: Intertwined helices
Layer 10

## Slide 9: Compact Arbitrary Superconducting Polarization Emitting Radiator

## Slide 10: Compact Arbitrary Superconducting Polarization Emitting Radiator
Changing current direction

## Slide 11: Compact Arbitrary Superconducting Polarization Emitting Radiator
With a circular field amplitude of 1T, the K value remains above 2.0 for a period length of 15mm

## Slide 12: Compact Arbitrary Superconducting Polarization Emitting Radiator
Gap of 6mm
Assuming constant current of 320 A (80% of Ic at 2T)
Chart: Period length (mm)
| 15 | 20 | 25 | 30 | 38
Bmax, circular (T) | 0.947 | 1.332 | 1.613 | 1.817 | 2.033
Notes: Mention that Athos 38mm, Porthos aims at 25-30 mm, Aramis afterburner 15mm

## Slide 13: Compact Arbitrary Superconducting Polarization Emitting Radiator
Winding, liquid nitrogen testing, splicing
Test facility and measurements
10 periods prototypes, 1 meter-long prototype
2026
2028
SwissFELplus pre-project
Specifications
Parameter | Values relaxed | Values optimal
Gap | 6 mm | 6 mm
Period length | 38 mm | 15 mm
Field amplitude | 2-4 T | 1-2 T
Keff values | 9.9(circular) - 14 (linear) | 2(circular) – 2.8 (linear)
Temperature | 4.2 K | 4.2 K
Notes: Mention relaxed parameters for first prototypes, then more realistic ones for Porthos and finally towards hard X-ray variable polarization

## Slide 14: Compact Arbitrary Superconducting Polarization Emitting Radiator
Main challenges :
Magnetization currents
Design of the end terminations
Small bending radius (<3mm)
Alternating local thicknesses between crossing points and straight segments
Insulation

## Slide 15: CASPER : Magnetization currents
Single helix powered

## Slide 16: CASPER : Magnetization currents
Single tape layer produces circular field of 20 mT
Single helix powered

## Slide 17: CASPER : Magnetization currents
Magnetization currents reduce the field by ~20%
-
=
Single helix powered

## Slide 18: CASPER : Magnetization currents
Two helices powered

## Slide 19: CASPER : Magnetization currents
Nonzero (~3%) perpendicular field
Two helices powered

## Slide 20: CASPER : Magnetization currents
-
-
=
All tapes powered
Left-handed powered
Right-handed powered
Magnetization currents
Two helices powered

## Slide 21: CASPER : Magnetization currents
Total
Left helix
Right helix
Magnetization currents
Magnetization effects account for <1% of Bx
Two helices powered

## Slide 22: CASPER : Magnetization currents
Using 250 A in inner helix and 270 A in outer helix, Bx is suppressed (<1% of By)
Two helices powered

## Slide 23: Compact Arbitrary Superconducting Polarization Emitting Radiator
Main challenges :
Magnetization currents
Design of the end terminations
Small bending radius (<3mm)
Alternating local thicknesses between crossing points and straight segments
Insulation

## Slide 24: CASPER : End terminations
Option 1: Looping each tape back
Credit: S. Richter, PhD thesis 2023
Current leads
HTS splices
Option 2: Splicing each tape layer in series
Notes: Stress the fact that tapes need to be bended such that HTS is under compression

## Slide 25: CASPER : End terminations
Option 1: Looping each tape back
Advantages:
  Continuous winding
Disadvantages:
  Complex geometry
  May create dipole
  Limited length
Credit: S. Richter, PhD thesis 2023

## Slide 26: CASPER : End terminations
Current leads
Option 2: Splicing each tape layer in series

## Slide 27: CASPER : End terminations
Option 2: Splicing each tape layer in series
B. Krasch, F. Abusaif, T. Arndt, N. Glamann, A. Grau, and D. S. de Jauregui, IEEE Transactions on Applied Superconductivity, vol. 34, no. 5, pp. 1–4, Aug. 2024

## Slide 28: CASPER : End terminations
Current leads
Helices connected in same layer
Option 2: Splicing each tape layer in series

## Slide 29: CASPER : End terminations
Current leads
Tapes connected to layer above/below
Option 2: Splicing each tape layer in series

## Slide 30: CASPER : End terminations
Advantages:
  Easier to bring tapes out of coil
  More scalable
Disadvantages:
  Requires ~800 low resistance joints
  Heat buildup
Option 2: Splicing each tape layer in series

## Slide 31: Compact Arbitrary Superconducting Polarization Emitting Radiator
Main challenges :
Magnetization currents
Design of the end terminations:
Small bending radius (<3mm)
Alternating local thicknesses between crossing points and straight segments
Insulation

## Slide 32: CASPER : Minimum bending radius
~82% critical current reduction for CORC winding
T. Mulder et al., IEEE Transactions on Applied Superconductivity, vol. 28, no. 3, pp. 1-4, April 2018, Art no. 4800504
Single tape minimum bending radius of ~2mm
S. Richter et al., Proceedings of the 12th International Particle Accelerator Conference, vol. IPAC2021, p. 4 pages, 2021

## Slide 33: Compact Arbitrary Superconducting Polarization Emitting Radiator
Main challenges :
Magnetization currents
Design of the end terminations:
Small bending radius (<3mm)
Alternating local thicknesses between crossing points and straight segments
Insulation

## Slide 34: CASPER : Crossing points spacing
Tapes stacked on each other
Spacing between tapes

## Slide 35: Compact Arbitrary Superconducting Polarization Emitting Radiator
Main challenges :
Magnetization currents
Design of the end terminations:
Small bending radius (<3mm)
Alternating local thicknesses between crossing points and straight segments
Insulation

## Slide 36: CASPER : Insulation
Faster current ramping
Lower current density
Complicated quench protection
Slow ramping time
Possible current sharing
Easier quench protection
Full insulated
Non-insulated
Hwang YJ et al., Applied Sciences. 2020; 10(5):1564

## Slide 37: Conclusion
CASPER undulator promises high field at small period lengths with variable polarization
Several challenges need to be overcome:
    Magnetization currents
    Winding and end terminations
    Minimum bending radius studies
    Spacings between tapes
    Insulation

## Slide 38: Compact Arbitrary Superconducting Polarization Emitting Radiator
Assuming constant current of 320 A (80% of Ic at 2T)
Tape thickness variation
K. Tsuchiya et al., Cryogenics, vol. 85, pp. 1–7, Jul. 2017
perpendicular