## Slide 1
S. M. Liuzzo
On behalf of the EBS Accelerator Team and the international collaboration:
SLAC, INFN, CERN, PSI, CORNELL
6GeV Linac and COLD project: beam dynamics and planning
(COLD) Cool copper Operation Linac Demonstrator

## Slide 2: ESRF injectors upgrade
Robust long term operation of the facility: Complete renewal of obsolete injectors providing low emittance injected beams (<1nmrad, >40 times smaller than the present injectors, <1mm bunch length >10 times shorter bunch, 0.6mA/bunch)
Enable future upgrades of the storage ring: Enable ultra-low emittance / low aperture / low gaps SR lattice design by relaxing constraint on DA.
Enable new opportunities making use of the linac electron beam (short pulse facility, FEL)
Large investment  staged implementation with minimal shutdown period
Most cost effective solution (investment, operation and maintenance)

## Slide 3: Advantages of a low emittance injector
Booster beam
Linac beam
x
t
x
stable space
standard off-axis, on-energy
on-axis,
off-phase
stored beam
t
2ns, 2mrad kicker
60nm x 17mm
1nm x 1mm
*M.Aiba: https://journals.aps.org/prab/abstract/10.1103/PhysRevSTAB.18.020701
Demonstrate state-of-the-art compact technology for users facilities injectors
Enable transparent on-axis off-phase * accumulation with ultra short injected beam (with ultra-fast kicker).
ESRF is presently considering a complete upgrade of our injectors with a full energy linac: limited space available, high gradient technologies could be a solution
not to scale

## Slide 4: A 65pm H9BA lattice could operate with a linac injector beam
Energy: 6 GeV
Energy loss / turn: 2.61 MeV
Mode emittances: 65 pm rad (flat beam)
Energy spread: 0.0014
Bunch length: 4.0 mm
Cavities voltage: 6 MV
Lifetime: 15 h
Not trivial even for a linac injector to obtain 100% inj.eff.
No errors
H9BA optics (SSRLX, P.Raimondi) with in addition reverse bends. No injection section (exists).
Booster upgrade
Linac
X [m]
85cm separate 2 bunches, injection at 1/3 =28cm
Fast kicker

## Slide 5: A 50pm 12 bend EBS lattice could operate with a linac injector beam
Energy: 6 GeV
Energy loss / turn: 2.23 MeV
Mode emittances: 50 pm rad (flat beam)
Energy spread: 0.000976
Bunch length: 3.06 mm
Cavities voltage: 6 MV
Lifetime: 38h
EBS_UP 2a3 , P.Raimondi, March 2025
Optics matched at IDs, ~12 Bend Achromat
Quad gradients up to 150T/m
Could profit of a linac injector to get 100% transparent inj.eff.
No errors
Booster upgrade
Linac
X [m]
Fast kicker

## Slide 6: A 34 pm 12+bend EBS lattice could operate with a linac injector beam
Energy: 6 GeV
Energy loss / turn: 2.13 MeV
Mode emittances: 34 pm rad (flat beam)
Energy spread: 0.0019
Bunch length: 7.5 mm
Cavities voltage: 6 MV
Lifetime: 37 h
EBS_UP 2a3 + reverse bends
Could profit of a linac injector to get 100% transparent inj.eff.
No errors
Booster upgrade
Linac
X [m]
Fast kicker

## Slide 7: Final Objective: 100% transparent injection for users
Bunch length = 2mm
1/1 nm.rad
Peak I.E. = 99.9%
6GeV LINAC
 | Booster | Linac
Technology | Well established /in-house expertise | Experimental, need to build expertise
Scientific reach | None | technological breakthrough (compact injectors)
Beam parameters | Low emittance / bunch length (~10 nmrad) | Ultra-low emittance bunch length (0.5 nmrad)
Power consumption | Same or higher as present | Factor 2 (?) lower (estimated)
Impact on injection performance | High efficiency accumulation | High efficiency accumulation
Dark time | 6month - 1 year (?) | ~ 2month + Long shutdowns
Cost | 44 Meuros: ~40 MEuros (from 3x SOLEIL booster) + 4 Meuros New standard technology linac (tunnel exists) | 53 Meuros (pulse compression) 68 Meuros (no pulse compression) (including tunnel)
operation | Complex (ramped EBS-type) | Complex (tbd with COLD project)
Fully transparent
(NLK or on-axis)
BEST Value for Money

## Slide 8: ESRF Main issue: SPACE
145m
Conventional ~15MV/m S-Band accelerating gradient LINAC: ~450m long
ESRF site (same scale):
A conventional full energy linac does NOT FIT on the ESRF site.
Not only reason to exclude this option:
more expensive
more consumption
many other laboratories already operate more advanced solutions
gun
Our present linac at 6Gev instead of 0.2GeV
e- @ 6GeV
gun

## Slide 9
E.Nanni, SLAC, IPAC, Venice, 2023
https://arxiv.org/abs/2203.09076
See E.Nanni’s presentation today

## Slide 10: 6GeV full energy LINAC: better beam, less consumption, same cost
Fits on site
X ”pushed” design
X High cost
V BEST SOLUTION
Lowest consumption
x25 = 100Hz 6GeV FEL power
Cost estimates compatible with Compact Light cost estimates.
Booster+linac
* From Soleil-II and Petra-IV estimates
SwissFEL and other linacs
Compact
Light
145m

## Slide 11: Can we reduce the number of klystron?
A single 50MW klystron, 4s pulse length with pulse compression could feed 2 cryomodules, 4 acc.struct (b=2) to get 75 MV/m for a single bunch
Thus reducing by almost a factor 2 the # of RF-units needed and consequently the overall price of the installation.
Usually 3ms. 4ms could be possible according to CANON.
80 MeV
80 MeV
50MW, up to 100Hz, 3ms
75 MeV
75 MeV
50MW, 4Hz, 4ms
75 MeV
75 MeV
Pulse compressor
(PSI-BOC, Q=220000)
30% of power reduction at the output of the BOC to take into account WG losses and some klystron power margin.
80 MeV
80 MeV
50MW, up to 100Hz, 3ms
1
2
3
1) Direct power from RF-units
2) Pulse compressor
SEE A.D’Elia this afternoon

## Slide 12: 6GeV linac 300MeV unit module must be 5.93m long at most
BPM inside quad
Acc. structures
Quadrupole
on movers
stripline
Compact Vaccum valve
bellow
bellow
328cm
7.8m
BPM inside quad
Acc. structures
Quadrupole
on movers
stripline
Compact Vaccum valve
Neutron monitor
bellow
bellow
278cm
Acc. structures
bellow
278cm
Screen
5.93 m
BPM inside quad
Acc. structures
Quadrupole
on movers
stripline
screen
Neutron monitor
bellow
bellow
PC
50MW
PC
50MW
4mm.mrad, ~400pmrad@6GeV
0.19% energy spread
0.5mm bunch length
6.444 GeV in 170m, 21 x 7.8m modules
5.6mm.mrad, ~500pmrad@6GeV
0.18% energy spread
0.5mm bunch length
6.159 GeV in 131m, 21 x 5.93m modules
Fits on ESRF site
Ideal 5.70 m
Based on SLAC’s cryomodule design and frequent diag and optics.

## Slide 13: A Shorter 300MeV unit module is needed for a 6GeV Linac
4mm.mrad, ~400pmrad@6GeV
0.19% energy spread
0.5mm bunch length
6.444 GeV in 170m, 21 x 7.8m modules
5.6mm.mrad, ~500pmrad@6GeV
0.18% energy spread
0.5mm bunch length
6.159 GeV in 131m, 21 x 5.93m modules
Fits on ESRF site
⚠️
Smaller values likely following recent updates.
Simulations done with RF-Track
https://abpcomputing.web.cern.ch/codes/codes_pages/RF-Track/

## Slide 14: Power consumption
Parameter | Value
RF Power [MW/m] | 22.5
Klystron Power [MW] | 50
Klystron Power Lost [MW] | 5
Number of Structures | 80
Number of Klystrons | 40
RF Source Efficiency [%] | 40
Modulator Pulse [microsecond] | 3
Modulator Power [MW] | 125
Energy / Pulse [J] | 375
Rep. Rate [Hz] | 10
Power / Modulator [kW] | 3.75
Electrical Power [kW] | 150
Parameter | Value
Energy Per Pulse [J/m] | 23
Rep. Rate [Hz] | 10
Thermal Power [W/m] | 230
Thermal Leakage [W/m] | 20 (overestimate)
Number of Structures | 80
Cryo Thermal Load [kW] | 20
Cryogenic Cooling Efficiency [%] | 15
Electrical Power for Liquifier [kW] | 135
Flow [l/s] | 0.1
from E.Nanni: https://indico.esrf.fr/event/173/#1-consumption-evaluation-for-e
2 min fill time per hour = 120 s per hour
24 liter per hour LN2
<5% duty factor
Flow rate is very low
Operate cryocooler at 5% of peak demand to match duty factor
15 kW for cryocooler
peak power 165 kW, 15 kW continuous
Annual power
~15 kW average (5% of 285kW)
5000 h operation
75 MWh/year
ESRF site power: 6.6MW * 5000h (reference) = 33000 MWh/year
ESRF site power during injection: 7.5MW
ESRF present injectors power ~0.9MW * 167h (2min hourly refill) = 150 MWh/year
Large over-estimate: assumes a 100mA refill at every topup.
High gradient c-band 77K linac injector will consume less or equal compared to the present.
Total peak (RF + Cooling): 285 kW
100% duty cycle
+ The increase in injection efficiency (+30%) will further reduce the duty factor

## Slide 15
COLD
A demonstrator to prove
high gradient cryogenic accelerating structures
for users facility grade operation
at low repetition rate.
The pre-injector of a new 6GeV linac.
C2 cold copper
Operation
Linac
Demonstrator
4Hz
4Hz
Waveguide S-band
Photo-gun
modulator
25 (35) MW
1.5 ms
S-band (2.998GHz)
klystron
modulator
50 MW
4.0 ms
C-band 5.712GHz
Control PS
planar hybrid
isolator
laser
Alignment
Diagnostic
LN2
solenoid
pulse compressor
Vacuum pump
Waveguide C-band
SLAC’s C-band distributed coupling accelerating structures
Steerer
screen
Fast CT
Steerer
Vibration
Quadrupole
Screen
RF deflector
BPM/BLM
Beam dump
dipole
klystron
BPM/BLM
Quadrupole
Quadrupole
Quadrupole
BPM/BLM
Interlocks
PSS Safety
LLRF
If 6Gev linac is approved, this facility will become a conditioning/test facility and most components will be part of the 6GeV linac. If not approved remains C-band cryogenic RF test stand.

## Slide 16: INFN-LNF SPARC (or CTF2) photo-GUN:
SLAC distributed coupling standing wave cryogenic accelerating structures and cryomodule
PSI: Pulse compression
high charge,
small emittance, short pulse length
high gradient (135MV/m)
Low breakdown rates at 77K
Enabling technologies available from the international collaborators
CERN: simulation tools (RF-Track)
CORNELL: FEL options
High quality factor C-band RF pulse compressors
R.Zennaro et al. C-band RF Pulse Compressor for SwissFEL, IPAC2013
D. Alesini et al. https://doi.org/10.1103/PhysRevAccelBeams.21.112001
https://arxiv.org/abs/2203.09076
https://abpcomputing.web.cern.ch/codes/codes_pages/RF-Track/

## Slide 17: ESRF Liquid nitrogen network and storage
✓
NEARBY LN2 SUPPLY ~ 110.000 LITERS
(ALREADY USED BY BEAMLINES)
LN2 NETWORK TO BE EXTENDED TO LINAC TUNNEL
BEST CHOICE

## Slide 18: Space available
Present linac 19.5m
Empty tunnel space 40m
60m long tunnel
✓
✓
Safety
~0.5GeV C3 demonstrator could fit in the empty tunnel and allows independent EBS operation
The empty tunnel space will be used for conditioning of RF structures (S-Band, C-band, …), test of diagnostics, training of personnel with high-power, pulsed RF, UHV, laser technology…

## Slide 19: C-band Linac ~150-300 MeV pre-injector: OBJECTIVES
Accelerating Gradient
Breakdowns (10-7 /pulse /meter).
Acceleration in presence of a breakdown
Dark currents
Compact
Reliable, maintainable
alignment
Possible lower temperature reach
(need dedicated structure design)
Beam position
Yttrium laser
Radiation safety
RF deflector
Dipole
Radiation safety
Beam charge
steerer
3xQuadrupole
Vacuum valve
PC
50MW
4ms
4Hz
35MW
WP1
WP10
WP3
WP2
WP2
WP2
WP1
WP8
WP1
Low Level RF
S-band
C-band
WP9
Beam charge
Radiation safety
Radiation safety
Radiation safety
Cryomodule 3.3m
WP10
Beam position
Cryomodule 2.7m
Vacuum valve
Beam position
Beam position
Quadrupole
Beam energy
7MeV
150MeV
300MeV
steerer
Beam charge
Vacuum valve
ALIGNMENT
PULSE COMPRESSION
GUN
Solenoid
CRYOMODULE
BEAM PROPERTIES
HIGH CHARGE
Low emittance
HIGH GRADIENT
RF CONTROL
Vacuum valves
Vacuum valves
OBJECTIVES
Diagnostics
RF
Magnets
Infrastructure
Safety
Laser
Legend
Control
Control system
LONG PULSE
WP7
WP9
WP7
WP3
WP4
WP1
WP4
WP1
WP1
Hardware interlocks
Safety interlocks
Vacuum valves
Shot – shot reproducibility
Energy, Emittance
Bunch length, charge

## Slide 20: Phase 0 (NO ELECTRON BEAM)
Acc. structures
3xQuadrupole
on movers
stripline
Vaccum valve
Neutron monitor
bellow
bellow
1x 50MW C-band RF-unit
~3.9m
SLAC
50MW
Cryomodule
3.28m
Faraday cup
Faraday cup
SCREEN
BPM
OBJECTIVES:
High gradient (up to 50MW, 4us, 10Hz)
4us pulse from klystron
Clearing of dark currents
RISKS:
dark currents  quadrupoles forward
 struct. positions backward
Higher than expected breakdown rates
Experience gained:
QCM operation
C-band in- vacuum RF distribution
LLRF for conditioning and breakdown count

## Slide 21: Phase 1
Hardware protection Interlocks
Personal safety Interlocks
GUN
SOLENOID
on movers
HV corrector
SCREEN
From Compact Light CDR
destructive
sparc-mm-06/001
Current transformer
BPM
Vaccum valve
laser optics table
Laser input
Radiation monitor
Dipole
shielding
SCREEN
Faraday cup
BPM
Radiation monitor
Acc. structures
3xQuadrupole
on movers
BPM
Vaccum valve
Radiation monitor
bellow
GUN SECTION
DIAGNOSTICS SECTION
Radiation monitor
bellow
PC
SLAC
50MW
35MW
Cryomodule
3.28m
Control system
Low Level RF
S-band
C-band
SCREEN
destructive
SCREEN
destructive
BPM
Current transformer

## Slide 22: Phase 1
GUN
SOLENOID
on movers
HV corrector
SCREEN
From Compact Light CDR
destructive
sparc-mm-06/001
Current transformer
BPM
Vaccum valve
laser optics table
Laser input
Radiation monitor
Dipole
shielding
SCREEN
Faraday cup
BPM
Radiation monitor
Acc. structures
3xQuadrupole
on movers
BPM
Vaccum valve
Radiation monitor
bellow
GUN SECTION
DIAGNOSTICS SECTION
Radiation monitor
bellow
PC
SLAC
50MW
35MW
Cryomodule
3.28m
Control system
Low Level RF
S-band
C-band
SCREEN
destructive
SCREEN
destructive
BPM
Current transformer
Hardware protection Interlocks
Personal safety Interlocks
OBJECTIVES:
High gradient (up to 240MW, 0.5us, 10Hz)
Beam 150MeV (or more, test limit 350MeV)
Beam properties
Beam properties in presence of breakdown
Pulse compression
RISKS:
dark currents  quadrupoles forward
 struct. positions backward
Higher than expected breakdown rates
Alignment  dummy cryomodule
Beam properties: energy, charge, emittance
Experience gained:
QCM operation
Beam tuning
Pulse compression
LLRF for pulse compression
S-band ~ C-band ~ Laser Synchronization

## Slide 23: Phase 2
GUN
SOLENOID
on movers
HV corrector
SCREEN
From Compact Light CDR
destructive
sparc-mm-06/001
Current transformer
BPM
Vaccum valve
laser optics table
Laser input
Radiation monitor
RF deflector
https://doi.org/10.1016/j.nima.2006.07.050
Dipole
shielding
SCREEN
Faraday cup
BPM
Radiation monitor
Acc. structures
3xQuadrupole
on movers
BPM
Vaccum valve
Radiation monitor
bellow
GUN SECTION
DIAGNOSTICS SECTION
BPM inside quad
Acc. structures
Quadrupole
on movers
Compact Vaccum valve
Radiation monitor
bellow
bellow
bellow
PC
SLAC
Short
50MW
35MW
Cryomodule
3.28m
Cryomodule
2.7m
Control system
Low Level RF
S-band
C-band
SCREEN
destructive
SCREEN
destructive
BPM
Current transformer
1x “6GeV linac 300MeV module”
Hardware protection Interlocks
Personal safety Interlocks

## Slide 24: Phase 2
GUN
SOLENOID
on movers
HV corrector
SCREEN
From Compact Light CDR
destructive
sparc-mm-06/001
Current transformer
BPM
Vaccum valve
laser optics table
Laser input
Radiation monitor
RF deflector
https://doi.org/10.1016/j.nima.2006.07.050
Dipole
shielding
SCREEN
Faraday cup
BPM
Radiation monitor
Acc. structures
3xQuadrupole
on movers
BPM
Vaccum valve
Radiation monitor
bellow
GUN SECTION
DIAGNOSTICS SECTION
BPM inside quad
Acc. structures
Quadrupole
on movers
Compact Vaccum valve
Radiation monitor
bellow
bellow
bellow
PC
SLAC
Short
50MW
35MW
Cryomodule
3.28m
Cryomodule
2.7m
Control system
Low Level RF
S-band
C-band
SCREEN
destructive
SCREEN
destructive
BPM
Current transformer
1x “6GeV linac 300MeV module”
Hardware protection Interlocks
Personal safety Interlocks
OBJECTIVES:
Compact cryomodule
Accelerating structures designed for injectors
Validate Pulse compression scheme
Beam 300MeV
Beam properties + bunch length
Beam properties in presence of breakdown
Maintenance procedures
Stress tests
RISKS:
Cryomodule  use a second QCM if needed
Alignment  beam based structures alignment, laser shaping,
Higher than expected breakdown rates
Beam properties: energy, charge, emittance, length
Experience gained:
Compact Cryomodule operation
Pulse compression
LLRF for pulse compression
Laser~S-band~C-band~C-band Synchronization
Beam tuning
maintenance

## Slide 25: Layout in LINAC bunker and modulators hall

## Slide 26: Timeline for the COLD projecT
Date | Instrument added to the installation | Beam achievements | project
2026-Dec SD | ModS4- RF-unit (SAT) |  | Phase 0
2027-May SD | First C-band RF-unit |  | Phase 0
2027-Aug SD | First C-band Acc. Struct. |  | Phase 0
2028-May SD | Infrastructures installation |  | Phase 1
2028-May SD | Diagnostics and beam dump |  | Phase 1
2029-Jan SD | S-band photo-gun + laser | 7MeV photogun beam | Phase 1
2029-May SD | Beam in Acc. Struct. | 150MeV beam (expected 150) | Phase 1
2030-May SD | RF deflector | 2ps bunch length | Phase 1
2029-Dec SD | Second C-band RF-unit (if needed) and new injector design acc.struct |  | Phase 2*
2030-Sep |  | 300MeV beam (expected 300) | Phase 2*
2031-Aug SD | TL1upgrade and inject in booster | 300MeV beam to booster | Phase 3*
* No planning or budget at the time being
Delivery Jan 2026
SAFETY authorization for Phase 0, 1, 2, 3
EIC proposal for Phase 0, 1, 2
Budget and planning for Phase 0, 1
CFT April 2026

## Slide 27: Beam dynamics: Initial part of the linac (up to 150MeV) = COLD Phase 1
5.5 mm.mrad , 2.0 ps
desired: ~5mm.mrad, 0.5ps
700pC
SPARC 3GHz gun
Cu cathode
120 MV/m
sr = 0.6 mm (uniform)
st = 200 fs (gaussian)
Bz = 0.29 T
Ez C band = 135.0MV/m
~1 m drift for diagnostics
Simulated particle emission
Space charge
gun
Acc. struct.
in cryomodule
Diag. section and beam dump
Diag. section
⚠️
S.Bettoni from PSI noticed that the emittance value is about ~5 times larger than expected.
PhysRevSTAB.18.123403

## Slide 28: Collaboration working on emittance simulations differences RF-Track - ASTRA
Wei-Hou Tan, SLAC
G.J.Silvi, INFN
SITF
SITF
200ps
SITF
700pC
In ASTRA simulations, emittance is ~ 1 mm mrad

## Slide 29: RF-Track simulations
Final 4d emittance at linac start = 1.05 mm.mrad; at linac end 1.08 mm.mrad
A.Latina, CERN
1) interpolate 1D fieldmaps on a regular 1D mesh, 2) smoothing function similar to that used in Astra 3) fund a better working point using Bayesian optimisation in Xopt to get a small emittance at the entrance of the first linac structure using the gun phase and the solenoid field as degrees of freedom.
sr = 0.3 mm (gaussian)
st = 2.79ps (gaussian)
0.289795 T
Different optimal parameters.
0.823 m gunlinac

## Slide 30: Error studies (6GeV linac)
50 um alignment: RF, BPM, Quadrupoles
1 deg random phase error among structures
Latest simulations do not show as good results
5 mm.mrad input beam emittance
3.55mm iris,
compact cryomodule length,
updated field on axis,
include 0-100MeV space charge dominated sections.
2025, 5.24mm iris, 2 mm.mrad
⚠️
2026

## Slide 31: Errors sensitivity: quadrupoles
Error sensitivities are very forgiving. ~1% emittance growth for 1 micrometer random errors (vibrations)
Plot style and analysis inspired from Wei-Hou Tan et al., Emittance Preservation in the C3 Main Linear Accelerator, SLAC, submitted for publication
Since emittance is not critical, we must check also corresponding beam position jitter amplitude that could harm later transport chain and finally injection efficiency.
15 nanometers for C3 collider

## Slide 32: Planning, HR and WP organization @ ESRF
Including resources and following an almost flat financial profile is set up with the available tools (excel mainly).
~200 tasks
30 people
WP-01 RF
WP-02 Diagnostics and Laser
WP-03 Vacuum
WP-04 Mechanical Engineering
WP-05 Infrastructure
WP-06 Operation
WP-07 Controls
WP-08 Alignment
WP-09 Safety
WP-10 magnets
and power supplies
WP-11 beam dynamics
WP-12 Timing
A.D’Elia
F.Ewald
H.Pedroso Marques
T. Brochard
Y. Gouez
J.-L. Revol
R. Bourtembourg
C. Gonzalez Torres
P.Colomp
C. Benabderrahmane
P. Falaise
S.M.Liuzzo*
Not. Available
Q.Qin, P.Borowiec, S.White, J.-L.Revol
Management:
Human resources:
3-years contract for cryomodule design
3 years contract for diagnostics/laser
3 years contract for RF accelerating structures design for Phase 2 (could be a PhD)
3 years contract for mechanical engineering
Resources for Safety and Infrastructure (to be defined)
Needed:
Hiring:
1 COD selected for LLRF (3 years)
1 PhD open for Beam Dynamics (6GeV linac)
1 COD to be opened for high power RF (3 years)
* project coordination

## Slide 33: BUDGET
S-band RF unit
C-band RF unit,
infrastructure
Diagnostics, waveguides, laser, acc. structures
Photo gun,
Pulse compressor
RF deflector
Financial profile and budget codes are set up
High power RF measurements
Beam
infra
RF
DIAG
BUDGET EVOLUTION:
April 2025: ~5M€
June 2025: ~6.0M€
October 2025: ~6.5M€
+ Infrastructure, RF-deflector
+ Detailed inputs from all WPs
+ updated costs
6.5MEuros total to reach Phase 1:
- 250 k€ refilling QCM with 300l dewars
- 250 k€ if we can leave without RF-deflector
+100K

## Slide 34: European commission EIC grant application
We are applying to EIC Pathfinder Open
Deadline for submission 12th May 2026 (open 5th February ‘26)
High risk - high gain project
Bring technology to no more than TRL4 (Technology validated in lab)
22 pages to be filled in: Excellence, Impact ( applications other than basic science, could be medicine, industry), Quality, budget.
Lump sum payments, budget pre-approved, advance payments and residual at WP finalization.
2.1% success rate last year (likely will need to resubmit next year)
4-5 labs, 5-7 WPs, SLAC can be an associated partner
For people-travel-consumables not for hardware
4 millions over 60 months
ESRF
INFN
CERN
SCANDINOVA
Instrumentation Technologies
SLAC (Associated, no budget)
Submission
7th May 2026

## Slide 35: rough draft timeline f0r EIC proposal
Tasks and Budget FROZEN.
Only editing phase.
Lump sum = payment at each WP conclusion  WP must be staggered
T0 could be October 2026
planning linked to COLD project master planning
BENKEI company hired for 2x project review. Last review will take place in 24th April.
Could finance 4 additional HR for: Cryogenics, Laser, RF, Mechanical Engineering (phase 2 cryomodule)
2% success rate in 2025
Includes: Alignment dummy cryomodule
Phase 2 cryomodule
T0=2026
Tend=2031
3 person/month spent to prepare this proposal

## Slide 36: Collaborations set up and other sources
ESRF – SLAC: works started in May 2025. Difficult to sign a collaboration contract as for EU partners. SLAC as an ESRF user also discarded. Latest option under evaluation: international CRADA
ESRF – INFN: agreed to purchase the photo-electron-gun via a Call For Tender. Collaboration Frame contract renewal in the hands of the DG office. Should be based on the previous contract. Addendum will detail the COLD project collaboration terms.
ESRF – PSI: agreed to purchase the BOC pulse compressor (CFT or as part of the collaboration contract). Collaboration Frame contract renewal in the hands of the DG office. Should be based on the previous contract. Addendum will detail the COLD project collaboration.
ESRF – CERN: discussion started.
ESRF – CORNELL: informal collaboration.
GEAR-NG Proposal for MSCA staff exchange includes travel for COLD to SLAC and INFN (~40kEuros). SOLARIS JU asked to travel to ESRF to participate in commissioning of COLD linac.

## Slide 37: INFN Visit FEbruary 2025
Loads to test modulators+klystron
(4x titanium 3D printed spirals)
Low loss circular waveguide and mode converters for long distance (here x-band)
Last laser mirror MUST BE OUT OF VACUUM
( critical hardware, often needs to be replaced)

## Slide 38: INFN Visit FEbruary 2025
PSI C-band BOC (barrel open cavity) Pulse compressor (~60kEuros)
Laser Clean room (50-100KEuros)
Not needed for selected laser

## Slide 39: X-BAND Structure used for simulations in RF-TRACK
https://ieeexplore.ieee.org/document/9991980
Small Prototype: Active part ~ 50% of total
This structure is in Frascati now!

## Slide 40: CERN Visit November 2025
Same gun as proposed for COLD (2.998GHz)
Solenoid on movers
Laser beam imaged as on the cathode
Specrometer after the gun
Local handling for klystron
Unused Waveguide cooling
RF-Deflector
Dipole at the end of the line
Laser beam inside vacuum chamber for alignment

## Slide 41: PSI Visit January 2026
16mm Vacuum chamber
Modulator hall
Passive Streaker
Cooling infrastructure
RF deflector
BOC
Pulse compressor
C-band 40MeV/m linac

## Slide 42: MAX IV visit March 2206
Easy handling of klystrons
No S-band RF-units radiation
shielding
Waveguide clamping.
Buy better waveguides.
In-air last mirror before cathode
Thermal stability. Linac ALWAYS on.
Shielding to protect Modulators IGBTs
RF signal from first RF unit. Phase stability.
Very few quadrupoles

## Slide 43: Many High gradient linac facilities and projects (incomplete list)
All FELs: EuXFEL, SwissFEL, FERMI, etc...
Compact Light (https://www.compactlight.eu)
Eupraxia (https://www.eupraxia-facility.org/)
VIGAS (commissioned in 2024)
PETRA (Laser Plasma Accelerator, ESLS 2024)
FCC-ee injector (FCC Week 2023, 5-9 June, London)
We are not alone

## Slide 44: IHEP CEPC: C-band high gradient structUres, very similar to the C3 ones
For CEPC injector (100km collider, competitor of FCC)
100Hz, 1.5nC, 1-2 bunches, 6.4nmrad.
Everything is done in house. Very similar to our plans, missing the gun and the electron beam.
distributed
HG2025, Merida Mexico

## Slide 45: IHEP CECP
HG2025, Merida Mexico
« CEPC linac injector development in EDR and C3 technology development », Jingru Zhang , IHEP, April 2026

## Slide 46: CEPC linac injector COmpleted Phase 0 and planning for Phase 1
« CEPC linac injector development in EDR and C3 technology development », Jingru Zhang, IHEP, April 2026

## Slide 47: RADIABEAM
GRIT (inverse Compton scattering)
Very similar to our COLD project, but no cryogenics.
Manufactures of C-band components and accelerating structures.
Test stand for Cryo-high power (no beam).
Ku-band linac (15GHz)
HG2025, Merida Mexico

## Slide 48: Cornell proposal
AFSOR+NSF workshop Feb 2026

## Slide 49: Many thanks for your attention
S.Liuzzo on behalf of the COLD project team:
A.D’Elia, P.Borowiec, V.Serriere, M.Dubrulle, M.Morati, S.White, F. Ewald, N.Benoist, K.Scheidt, B.Roche, C.Benabderrahmane, G. Le Bec, R. Bourtembourg, J.-L. Pons, D. Martin, C. Gonzalez Torres, B. Pelissier, L.Eybert, T.Brochard, C.Maccarrone, J.-L. Revol, B.Joly, Y.Gouez, F.Favier, H. Pedroso Marques, P.Colomp, H.Gonzalez, A.Dely, F.Falaise, David Frichet, E.Mitchell, R.Gibson, D.Flood, A.Talucci, P.Lean, A.Dely, Q.Qin
International collaborators
E.Nanni, A.Dhar, W.-H. Tan, G.Aymar (SLAC),
A.Latina (CERN),
D.Alesini, F.Cardelli, A.Giribono, C.Vaccarezza, G.Silvi (INFN-LNF),
M.Andorf, J.Maxson (Cornell),
P.Craievich, R.Zennaro (PSI)
Special thanks to ESRF management and other divisions, for their support to the COLD project
6GeV Linac injector
Thank you for your attention!

## Slide 50: WP-01 RF
Definition of the RF power distribution, pulse compression studies, etc..
S-Band RF-unit purchased for photo-gun.
Fully compatible (identical) to the new RF-Units purchased for the present linac refurbishment.
In case COLD project is delayed, this equipment can be used for USM operation.
1 COD position open to hire a person to work on COLD project LLRF
1 COD position for high power RF (needed)
First component of COLD project purchased in 2025
Many thanks to the purchase office and all those who participated

## Slide 51
Ideal solution: Pharos 2H-4H from Light Conversion
  Diode pumped Yb-crystal laser (l = 1030 nm) with integrated 4th harmonics generation:
This laser is already used as UV-photon source for at
DESY (S-band photoinjector at SINBAD-ARES)
CERN CLEAR/CTF2 photoinjector
Photoinjector of CXFEL (Arizona State University)
= 257 nm
E = 100 - 200 uJ / pulse (*)
Single shot – 100kHz
Synchronisation to SSRF/4 (88 MHz)
Compact
827 cm
492 cm
25 cm
Positive feedbacks on performance and service (beam quality, stability, long term reliability,…)
190 fs
(*) depends on model
WP-02 diagnostics: Pharos 2H-4H from Light Conversion

## Slide 52: WP03-Vacuum
If possible we will follow SwissFEL vacuum design with 16mm inner vacuum tube diameter with CF40 flanges size CF
Linac pressure requirements lower than for Storage rings, 10-7 mbar range, like in our current installation.
Likely RF liners are not needed in single pulse. The issue is mostly coupled bunch instability, but impedance studies are certainly required.
This study needs to be done.
To achieve this pressure range baking the vacuum chambers and NEG coating is not needed. Not having to bake out the chambers simplifies the chambers supports design and reduce the requirements on bellows to accommodate the elongation of the vacuum chambers.
The vacuum valves will need RF Liners ?
Full metal gate valves ?
The SwissFEL shows that very low levels of radiation damage are expected and thus compact valves without full metal seals can be envisaged to be used.

## Slide 53: WP04- Mechanical Engineering
WP-04 Mechanical Engineering
Direct exchanges started between SLAC and ESRF teams.
3D modelling of the linac tunnel and modulator hall are taking place end of the year. A 3D model of the COLD project will be realized in the next months, according to what was planned.
A compact cryomodule design is needed for phase 2 of the COLD project.

## Slide 54: WP-05 infrastructure
Project analyzed in terms of:
Cooling requirements
LN2
Size and weights to be moved
Electricity requirements
RF equipments
Diagnostics
Control racks
Magnets
ISDD equipments (girders, supports, etc.)
Human resources

## Slide 55: WP-06 Operation
Gun
Bunch
C3_1
Gun
Laser
Mod S_4
Mod C1
C3_2
Diag &Optics
PC
325 MeV
325 MeV
Scandinova
Scandinova
Scandinova
Section 2
Section1
Mod S2
Mod S 1
Mod S0
Mod S3
overhead crane
Installation procedure: what enters and when.
Space for storage and handling solutions
Space availability in the PINJ modulator hall
Door separations

## Slide 56: WP-07 Controls
We could consider the preparation of a digital twin based on RF-Track simulations as the one of the EBS-SR to start creation of Device Servers and applications for control of COLD.
PRESENT LINAC
Interlocks: several WP involved RF, safety, operation, control, etc…

## Slide 57: WP-08 Alignment
Measurement of the earth embankment that covers the linac tunnel for SAFETY approval request to ASNR.
Linac
Modulators
hall
grass-covered earth mound
COMPLETED on 24th September 2025
Feb 2026  meeting to discuss cryomodule adaptation for alignment at ESRF

## Slide 58: WP-09 SAFETY
The procedure to obtain L'Autorité de sûreté nucléaire et de radioprotection (ASNR) approval requires drawings, simulations and a CDR document.
~2 years to obtain permission for beam. We are on schedule and started preparing the documentation.
6GeV Linac Injectors upgrade project is the ultimate justification for ASNR to approve COLD project
ASNR approval deadlines:
COLD authorization starts right after Linac Refurbishment
Prepare  6 months  Submit  1 year  Obtain (accelerators)
Submit  6 months (or less)  Obtain (klystrons)
1st Dec 2025: Prepare Drawings and beam information for Linac refurbishment (DONE)
Submit authorization for S-band RF unit (Klystron) (DONE)
1st July 2026: Submit authorization request to use RI structure as spare (not identical to present one)
Obtain authorization for S-BAND RF units (klystron)
2nd July 2026: Prepare Drawings and beam information for Phase 1-2-3-… Linac parameters 1000 part 6D beam at linac end
Submit authorization for C-band RF unit (Klystron) Phase 0
1st Jan. 2027: Submit authorization request for Phase 1-2-3
Obtain Authorization for C-band RF unit Phase 0
1st July 2027 : Obtain Authorization for linac refurbishement beam
1st Jan. 2028 : Obtain Authorization for beam and RF Phase 1-2-3-…

## Slide 59: WP-10 Magnets and Power supplies
More correctors needed (2) and quadrupole to be installed on mover or with integrated H/V correction coils
Included in the list of participants to the project also Power Supply Group.
2 H/V correctors (similar to the ones of TL1), 2028
1 quadrupole (similar to the ones of TL1), July 2027
1 dipole (similar to the ones of TL1), 2028
1 solenoid (the PS will likely be part of the photo-gun purchase), 2028

## Slide 60: WP-11 Beam dynamics: Initial part of the linac (up to 150MeV) = COLD setup
5.5 mm.mrad , 2.0 ps
desired: ~5mm.mrad, 0.5ps
700pC
SPARC 3GHz gun
Cu cathode
120 MV/m
sr = 0.6 mm (uniform)
st = 200 fs (gaussian)
Bz = 0.29 T
Ez C band = 135.0MV/m
~1 m drift for diagnostics
Simulated particle emission
Space charge
gun
Acc. struct.
in cryomodule
Diag. section and beam dump
Diag. section

## Slide 61: WP-12 Timing
This WP was recently added to the project.
2998.8 MHz
5712.0MHz
142.8MHz
X 21
X 40
GUN
Accelerating structures
352.372174 MHz
Storage Ring
Wait for coincidence within a given limit.
NO
NO
NO
GO!
EU S-BAND
C-BAND
COMPATIBLE WITH PRESENT LINAC

## Slide 62: COLD project risks
 | low | moderate | high | 6GeV show stopper | Impact USM
Lack of Human resources |  |  |  |  | 
Collaboration contracts / Amendments not established in time |  |  |  |  | 
Gradient not reached |  |  |  |  | 
Low reliability |  |  |  |  | 
Low repeatability |  |  |  |  | 
Low maintainability |  |  |  |  | 
Lack of financial resources |  |  |  |  | 
Pulse compression not reached |  |  |  |  | 
Module > 5.9m |  |  |  |  | 
Current not reached |  |  |  |  | 

## Slide 63: Conclusions
To upgrade the ESRF injectors, a full energy 6GeV linac is considered.
The shortest, cheapest and less consuming solution is a cryo C-band distrib. coupling acc. structure
High gradient technology leads to smaller footprint injector, thus reducing costs and fitting on site.
All components exist (no R&D needed). COLD project launched in April 2025 will prove the technology readiness and build the competences needed.
All Working groups are progressing on their tasks and in line with planning. HR hiring started.
A first draft Conceptual Design Report (~65 pages) is being prepared with deadline in April 1st 2026.
The documentation for the ASNR approval is being prepared.
In 2026 foreseen CFT of 50MW/4microsecond/4Hz C-band RF unit.
130m
50% of present
77K

## Slide 64: Backup slides

## Slide 65
Injectors
upgrade
SR Injection section
improvement
Booster
refurbishment
Linac
refurbishment
NEW
Linac
Non-linear injector kicker
Transparent injections
Maintain injection efficiency
Lower natural emittance
Higher injection efficiency in SR
Higher extraction efficiency
More reliability
Modernization
Higher energy
Advanced
design
✓
Procurement
✓
Advanced
✓
Short term
Long-term
Replace existing injectors with a full energy injector linac
Higher injection efficiency, lower injection perturbation, enable/facilitate future SR upgrades
6GeV + margin
> 600 pC (single bunch)
< 1 nm.rad at SR injection
< 0.1 % energy spread
< 1 mm bunch length
> 4 Hz repetition rate
Bunch spacing 2.8ns (in the SR)
Fits on site (maximum 180m)
As low energy consumption as possible
User facility grade :
Reliability
Reproducibility (turn on 1 month later and it works as before)
Maintainability easy to repair or operate with failing component for long term
3 M€
0.5 M€
1.5 M€
COLD
started
✓
5 M€
Mid-term

## Slide 66: Requirements For RF-photon-gun Drive Laser
Photo cathode material | Copper
Quantum efficiency QE for electron emission from Cu: | ~1 x 10-4
 Photoemission energy for Cu-cathode | 4.53 - 5.1 eV (different literature sources…)
 Laser wavelength in the UV | < 243 nm – 274 nm, e.g. 266 nm from 3rd harmonic of Ti:Sa e.g. 257 nm from 4th harmonics of Yb-based lasers
Electron bunch charge (wished) | 1 nC
 needed Laser pulse energy (4.3 eV * 1 nC/QE) | ~ 50 uJ on the cathode Losses during beam transport:  100 uJ minimum at laser output
Parameters defined by RF-cavity and Linac design | 
Laser pulse duration | ~200 fs
Laser spot shape and size on the cathode | 300 um radius, round flat top (maybe not needed)
Longitudinal pulse profile | gaussian
Other requirements | 
Repetition rate: | 4Hz… 10 Hz
Synchronisation capability | Phase locking to 1/4 SRRF (88 MHz)
Stability | High reliability and as much as possible maintenance free

## Slide 67: Beam Transport and Shaping
Wish list:
Transverse flat top profile on cathode surface, 300 um radius
? Variable pulse duration (190 fs – 2 ps)  UV pulse stretcher
Adjustment of beam dimensions (horizontal / vertical) on the cathode surface
Difficulties due to UV wavelength and short pulses (portential high intensities on/in optical elements)
Limited choice of materials for transmission optics and viewports (mainly fused silica)
Damage thresholds of optical coatings and bulk material to be taken into account
Carbon deposit on optical surfaces  influence on beam energy and profile
Total beam losses due to beam shaping and transport can be very high (> 60 %)

Choose pulse energy from laser with enough margin
Where possible use mirrors instead of lenses
As few optical elements as strictly necessary
Is the flat top transverse profile really needed? (ARES experience: maybe not needed)
Pulse stretching needed?

## Slide 68: WP04- Mechanical Engineering
WP-04 Mechanical Engineering
Direct exchanges started between SLAC and ESRF teams.
3D modelling of the linac tunnel and modulator hall are taking place end of the year. A 3D model of the COLD project will be realized in the next months, according to what was planned.
A compact cryomodule design is needed for phase 2 of the COLD project.

## Slide 69: Inj. Eff. in SR with 6GeV linac beam properties
Normal conditions beam at -8.mm
A. Sauret, PhD student, Beam Dynamics group
Bunch length = 2mm
1/1 nm.rad
Peak I.E. = 99.9%
Bunch length = 20mm
60/30 nm.rad
Peak I.E. = 82%
Booster (2025)
6GeV LINAC
Bunch length = 20mm
27/54 nm.rad
Peak I.E. = 92%
Booster (upgrade)

## Slide 70: ROUGH COST estimate based on Compact light CDR
Accelerator (6GeV) ~= 77 MEUR
FEL+beamlines ~= 94 MEUR
Infrastructure ~ = 60MEUR
Total FEL (6GeV) ~= 231 ± 60 Meuro
Accelerator (6GeV) ~= 77 MEUR
FEL+beamlines (3GeV, 50%*) ~= 47 MEUR
Infrastructure (3GeV, 50%*) ~ = 30MEUR
Total FEL (3GeV) ~= 154 ± 40 Meuro
Using the same data, removing bunch compressors and FEL buildings
Injector linac (6GeV) ~= 75 MEUR
Infrastructure ~ = 15MEUR (<1/3 of the buildings)
Total injector 6GeV ~= 90 ± 30 MEUR
Simpler injector and C-band acc.-struct. could also result in further economies
Injector linac (6GeV) ~= 56 MEUR
Infrastructure ~ = 7MEUR (<1/3 of the buildings/2)
Total injector 6GeV ~= 64 ± 20 MEUR
* 50% likely un underestimation, not linearly scaling
COMPACT LIGTH CDR: https://zenodo.org/records/6375645

## Slide 71: Power consumption
modified from E.Nanni: https://indico.esrf.fr/event/173/#1-consumption-evaluation-for-e
2 min fill time per hour = 120 s per hour
24 liter per hour LN2
<5% duty factor
Flow rate is very low
Operate cryocooler at 5% of peak demand to match duty factor
15 kW for cryocooler
peak power 165 kW, 15 kW continuous
Annual power
~15 kW average (5% of 285kW)
5000 h operation
75 MWh/year
Parameter | Value
Energy Per Pulse [J/m] | 23
Rep. Rate [Hz] | 10
Thermal Power [W/m] | 230
Thermal Leakage [W/m] | 20 (overestimate)
Number of Structures | 80
Cryo Thermal Load [kW] | 20
Cryogenic Cooling Efficiency [%] | 15
Electrical Power for Liquifier [kW] | 135
Flow [l/s] | 0.1
Parameter | Value
RF Power [MW/m] | 22.5
Klystron Power [MW] | 50
Klystron Power Lost [MW] | 5
Number of Structures | 80
Number of Klystrons | 40
RF Source Efficiency [%] | 40
Modulator Pulse [microsecond] | 3
Modulator Power [MW] | 125
Energy / Pulse [J] | 375
Rep. Rate [Hz] | 10
Power / Modulator [kW] | 3.75
Electrical Power [kW] | 150
ESRF site power: 6.6MW * 5000h (reference) = 33000 MWh/year
ESRF site power during injection: 7.5MW
ESRF present injectors power ~0.9MW * 167h (2min hourly refill) = 150 MWh/year
Large over-estimate: assumes a 100mA refill at every topup.
High gradient c-band 77K linac injector will consume less or equal compared to the present.
Total peak (RF + Cooling): 285 kW
100% duty cycle

## Slide 72: Realistic linac simulations including C3 cryomodule dimensions
C3 Cryomodule length = 3.28m
1 Acc.Struct. Length = 1.06 m
Phase 1
150MeV
Updated COLD simulations including all elements described above and full size QCM, for phase 1 and 2
Will update also full linac simulations, likely less energy margin and longer linac: 161m for a 6GeV linac. Instead of 110m for a 6.7GeV linac in previous simulations.
The cryomodule adds more than 1m to the over all length. A more compact design will be studied for the second module to be installed.
Phase 2
300MeV
Thanks to A.Latina for correction and improvement of the simulations scripts
5mm.mrad
9mm.mrad
Fixed using a triplet

## Slide 73: Cold copper collider parameters vs requirements for Injector linac
6GeV + margin
> 600 pC (single bunch)
< 1 nm.rad at SR injection
< 0.1 % energy spread
< 1 mm bunch length
> 4 Hz repetition rate
Bunch spacing 2.8ns (in the SR)
Fits on site (maximum 180m)
As low energy consumption as possible
User facility grade :
Reliability
Reproducibility (turn on 1 month later and it works as before)
Maintainability easy to repair or operate with failing component for long term
ESRF injector linac
C3
https://iopscience.iop.org/article/10.1088/1748-0221/18/09/P09040/pdf
Same gradient/effective gradient
Lower energy
(<180m instead of 8km)
4-10Hz instead of 120Hz
single bunch
0.66nC instead of 1nC
ESRF injector linac has RELAXED requirements compared to C3
But also more stringent ones:
High photo-gun charge
User facility grade :
Reliability
Reproducibility
Maintainability

## Slide 74: X-BAND Structure used for simulations in RF-TRACK
https://ieeexplore.ieee.org/document/9991980
Small Prototype: Active part ~ 50% of total

## Slide 75: SLAC distributed coupling accelerating structure
https://iopscience.iop.org/article/10.1088/1748-0221/18/09/P09040/pdf

## Slide 76: lifetime, injection efficiency and injector usage
EBS parameters:
Beam lifetime larger than 20 hours
Injection efficiency in the order of 70%
Top-up every 1 hour
Typical injection in 2022:
725 kW for the injector during 2 mn. every 1 hour
(45s for preparation, 70s for injection with only 32s beam on)
                 25 kWh
During machine development time, optimisation of the programme and guidelines is imposed for the usage of the injector.

## Slide 77: typical power consumption
One week operation:
Total electricity consumption of the institute:
4100 kW for the SR at 200 mA
+ 725 kW every hour for 2 mn for injection (1100 max with transient)
+ 2300 kW base facility consumption for labs, office, Experiments,…
+ 700 kW facility fluctuation for staff activity
854 kW Base with cooling and auxiliaries ON
Base Power in shutdown: 330 kW
360 kW HQPS consumption mode ECO:
(with transient up to 800 kW when SYRF switched ON )
In normal mode 510 kW (transient 731 kW).
2149 kW Power consumption of the storage ring without beam:
(Magnets: 1084 kW RF: Klystron: 941 kW SSA: 124 kW)
522 kW Beam power at 200 mA 150 kW ID power (90 kW average)
-------------
4035 kW Total for the storage ring
+725 kW Injector consumption (RF : 176 kW ; Magnets: 560 kW)
4100

## Slide 78: Operation issues
We assume linac cooling always on but no RF power in cavities except when linac is in use.
Our use case: 1 injection of 2 minutes every h (or more) for ~5000h per year.
If one structure breaks down for example at MAX-IV Short pulse facility (discussion with S.Molloy during ESLS2024 workshop) few shots are missed and few more are used to reach final tuning ramping nearby cavities to higher power. Always from their experience, the linac stays always on (used for users) to keep operational settings valid.
What are reliability and intervention time (warm up and cool down) of a cryomodule?
Cryomodule 77K
acc. struct.
Normal operation:
1 structure breaks down: more power in nearby structures, rematch of all downstream quadrupoles (if available sending settings to magnets could take few seconds, 1—30 shots lost for settings change.). Beam transport independent of cryomodule temperature? Keep magnets and diagnostics outside of cryomodule would be a better approach, simpler interventions and technology. Possible vacuum degradation.
77-300K

## Slide 79: Linac modules layout
Cryomodule 77K
acc. struct.
C3 like (may be wrong):
Cryomodule 77K
acc. struct.
300K
Possible layout for ESRF:
Initial part of linac
High energy part of linac
Diagnostics and magnets at room temperature, only accelerating structures in 2.3-2.5m cryo-modules.
Cryomodules are about the same length of ESRF invacuum-ID cryomodules.
Could also simplify alignment.

## Slide 80: Linac modules layout
9m long Cryomodules @77K
acc. struct.
C3 collider :
2.5m long Cryomodules @77K
acc. struct.
300K
Possible layout for ESRF:
Initial part of linac
High energy part of linac
Diagnostics and magnets are kept at room temperature, only accelerating structures in 2.3-2.5m cryo-modules.
In case of failure, retune neighboring magnets and structures.

## Slide 81: Other Light sources that use a linac as full energy injector
Spring-8-II

## Slide 82: Many High gradient linac facilities and projects (incomplete list)
All FELs: EuXFEL, SwissFEL, FERMI, etc...
Compact Light (https://www.compactlight.eu)
Eupraxia (https://www.eupraxia-facility.org/)
VIGAS (commissioned in 2024)
PETRA (Laser Plasma Accelerator, ESLS 2024)
FCC-ee injector (FCC Week 2023, 5-9 June, London)
We are not alone

## Slide 83: From HG2023 conference
350MeV linac
X-band
80MV/m (50MV/m)
Under commissioning near Beijing
Compatible with other ESRF injector projects
We are not building something totally new. High gradient accelerating structures linac has already been done.
We could have a similar scheme, with 50MW modulator and klystron + pulse compressors.
C-band

## Slide 84: High gradient technology
Q value & breakdown rate improvements
1985
1993
2017
2020
Varian
S-band, 77K, 1- cell, Q↗ ~2.7
MEPI (Russia)
  X-band, 77K, 1-cell, Q↗ ~2.5, 50MV/m
SOKENDAI (Japan)
C-band, 20K, High power, 1.3m, 30.9MV/m @ 1𝜇s
2016
2021
UCLA, SLAC (USA)
  X-band, 45K, 1-cell, 250MV/m, low BDR, Q↘@>150MV/m
SLAC (USA)
  X-band, New Structure, 300K, 20-cell, beam test 140MV/m
SLAC (USA)
  X-band, 77K, 20-cell, beam test 150MV/m，Q↗~2.25, 2 order of BDR lower
Mamdouh Nasr ,et al., PHYSICAL REVIEW ACCELERATORS AND BEAMS 24, 093201 (2021)

## Slide 85: Collaborations set up
High gradient accelerating structures
Cryomodule
photogun
simulations
FEL option
Simulations
(synergy in other projects, FCC injector)
Pulse compression
Existing Collaboration agreement
Started redaction of Collaboration agreement
RISK: if some of these collaborations fail to take place, end of project.
Informal collaboration
Informal agreement,
But may fall in existing collaboration agreement
Informal collaboration
But may draft an addendum as for fast kicker
Modulators maintenance

## Slide 86: Many High gradient linac facilities and projects (incomplete list)
All FELs: EuXFEL, SwissFEL, FERMI, etc...
Compact Light (https://www.compactlight.eu)
Eupraxia (https://www.eupraxia-facility.org/)
VIGAS (commissioned in 2024)
PETRA (Laser Plasma Accelerator, ESLS 2024)
FCC-ee injector (FCC Week 2023, 5-9 June, London)
We are not alone.
If ESRF does not want to fall behind, R&D and investment to produce a demonstrator would need to start now!!!

## Slide 87: Free Electron Laser
ESRF MAC Oct 2024:
Make a FEL, used as injector to motivate project with scientific drive.
1GeV
Undulator hall
beamlines
6GeV
40m long Ultra Compact XFEL
(undulators and beamline included)

## Slide 88: RADIABEAM
GRIT (inverse Compton scattering)
Very similar to our COLD project, but no cryogenics.
Manufactures of C-band components and accelerating structures.
Test stand for Cryo-high power (no beam).
Ku-band linac (15GHz)

## Slide 89: C3
Longer than I thought, actually assumed inner dimension instead of outer. But, space for Quad not needed.
One single opening
Hybrid inside the cryo-module.
STP file available

## Slide 90: INFN-LNF
Brazing free technology, powerfull cooling to tune each cell independently
MATURE TECHNOLOGY for S-band photo-gun
C-band gun installed at PSI

## Slide 91
Courtesy of L.Nadolski, SOLEIL
~13.2MEuro (2025)