## Slide 1: Water cooling “scheduling” and preliminary RF needs for the different COLD Phases
A. D’Elia

## Slide 2: SAT & Phase 0
 | Jan 2027 |  | July 2027 |  | After July 2027 – End 2027 |  | 
 | SAT S-Band RF Unit |  | SAT C-Band RF Unit |  | COLD - Phase 0: RF Cond. and test of SLAC struc. |  | 
SAT S-Band | Load SAT: 5l/min (3.15kW1) | RF Unit: 91l/min (P<5bar@91l/min) |  |  |  |  | 
SAT C-Band | - | - | Load SAT: 6l/min (4kW2) | RF Unit: 123l/min3 (P=5bar@123l/min) |  |  | 
Phase 0 | - | - | - | - | C-Load: 0.5l/min (300W4) | C-RF Unit: 123l/min3 (P=5bar@123l/min) | C-RF Wind.: 1x3l/min5
Tot | 96 l/min & 3.15kW |  | 129 l/min & 4kW |  | RF=126.5 l/min NB: All quads will be air cooled |  | 
1 Assuming T=10deg and 35MW*4.5us*20Hz.
2 Assuming T=10deg and 50MW*4us*20Hz.
3 Preliminary communication from Scandinova, not yet the real value that most probably will be lower (for S-Band the preliminary value was 113l/min).
4 Here we are NOT considering the pulse compression scheme that could be not yet available (see next slides).
5 The idea of putting RF windows close to the input of the cavities has been aborted: as commented by PSI colleagues putting a ceramic window in a region subject to very high fields and huge thermic stresses between cold and warm parts, is more a risk than a solution. However it could be useful to have a RF window allowing to intervene (for calibration for ex.) on the Directional Coupler at the output of the klystron without touching the vacuum of the whole installation. If that has to be cooled down or hasn’t, it is not clear (in case of SF6-vacuum separation the cooling is not needed). Here I put the worst case using the value given in the S-Band RF Unit for cooling the RF Window.
Discussing with Marc, we may (ONLY FOR SATs!) steal the water from Mod0. This possibility must not impact the run test of Mod0 on the Linac Section! Additional: what about electrical power? Earthing to be provided this year: Summer SD?

## Slide 3: C-Band: Phase 0 without pulse compression
load
C3 1m struct
C3 1m struct
DC
DC
C3 1m struct
50 MW
2ms, 10Hz
C-band
Planar hybrid
Atten
Ph.
Shift
Atten
PrefAv=300W
PKlysAv=1020W
PdissAv=727W
Considering that str=2, and a margin of 30% additional power for waveguide losses, all 50MW are needed without BOC. But with only 2us we can reach the nominal 80MV (Vmax=81.6MV reached after 3us).
Being an overcoupled SW structure: full reflection at the beginning of the pulse, some permanent reflection during the pulse, largest peak reflected power at the end of the pulse  Planar hybrid with load is needed.
2nd Half 2027
PrefAv=403W
PKlysAv=2020W
PdissAv=1035W

## Slide 4: Considerations on the hybrid scheme
C3 structures are SW this means that:
A reflected power will be present at the beginning and at the end of each filling pulse;
A constant reflected power will be present during the pulse when the structure is overcoupled (as it is in our case).
The planar hybrid will provide to zero reflection back to the klystron only if:
The “cavity waves” are in quadrature;
The “cavity wave” modules are equal.
This implies that we need a fine control of the phase and amplitude from the cavities. I am a bit worried about that…
Im
Re
Cav1
i Cav2*
Cav1+Cav2
Cav1
Cav2
If Cav1=Cav2  Port1=0
= If Cav2*Cav1 =
Planar Hybrid S-Matrix
Input
Output
Feeding from cavities
Typical return loss values for klystrons are 20dB  for 50MW, ~500kW Pref allowed
Port 1
Klys
Port 2
Cav1
Port 4
Cav2
Port 3
Load
Feeding from cavities
Planar hybrid
Note that the quadrature sign matters: Cav1 and Cav2 must be at +/2 as in the phasor diagram here on the left. In this case Port1=Cav1-Cav2. If they are at -/2: Port1=Cav1+Cav2!!
See next slide

## Slide 5: Some calculation on the hybrid scheme
Phasor Diagram

At the output of Port 1, towards the klystron:
(=0 in the diagram on the left)
Pref klys=0 only if A=B and = /2
(The module of the sum is independent on )
The voltage phasors entering in the ports 2 and 4 come from the reflection from the cavities and their modules will be proportional to the square root of PRef_Tot/2. The power flowing back to the klystron out from the Port 1 will be  . Considering the worst scenario (Phase 0 with PRef_Tot=70MW), here below a quick analysis in case of mismatching in amplitude and/or in phase:
=90; Pref1=35MW; Pref2=27MW  /10% or V/V11%
=83; Pref1=Pref2=35MW  /8%
=84; Pref1=35MW; Pref2=30MW
/5% or V/V7%; /<7%

## Slide 6
 | Components | Comments
Waveguides x C-Band | Planar Hybrid | 
 | C-Band Load | 70MW peak power, 300W average Power
 | 2 x Dir. Coupler C-Band | 
 | Phase shifter | 
 | Attenuators | 
 | Cables+electr. | 
Vacuum x C-Band | IP+electr. | 
 | Gauges+electr. | 
 | Vacuum valves (?) | In this way we won’t vent the cavity for the next phases.
Components needed for Phase 0 (2nd half 2027)
Of course we need also the waveguides but w/o drawings we can’t fix the layout. Delay for delivery tbd with PSI or with a Company if we want to profit for a qualification. With a Company I think that the leadtime should be at least 6 months if we don’t need special components (twists, particular bends…). PSI told us that they paid for waveguides 100kEuros/5m (several years ago): do we need a CFT?

## Slide 7: Phase 1
 | 2028 |  |  | 2029 |  |  |  |  |  |  |  | 
 | RF Gun Conditioning and Test |  |  | COLD – Phase 1: 150MeV beam acceleration |  |  |  |  |  |  |  | 
Gun RF Conditioning and Test | Isolator: 3.5l/min (P=2bar@nom. flowrate) | S-RF Unit: 91l/min | Load Isolator: 5l/min (0.45kW1) (P=2bar@nom. flowrate) |  |  |  |  |  |  |  |  | 
Phase 1 | - | - |  | Isolator: 3.5l/min (P=2bar@nom. flowrate) | S-RF Unit: 91l/min | Load Isolator: 5l/min (0.38kW2) (P=2bar@nom. flowrate) | C-RF Unit: 123l/min | C-Load: <0.5l/min (210W3) | C-RF Wind.: 1x3l/min | Dipoles: 1.5l/min (1.04kW) | Solenoid: 5l/min (10kW) | +Defl. Cavity Load(s): 5l/min (<150W)
Tot | ~100 l/min & 0.45kW |  |  | RF=226 (+10 for BOC) l/min + Magn.=6.5 l/min & 11.04kW (Def. Cav +5l/min & +0.15kW) NB: All quads will be air cooled |  |  |  |  |  |  |  | 
1 The isolator is dimensioned to work at 30MW*1.5us*10Hz=450W;
2 In operation the RF gun should need 25MW*1.5us*10Hz=380W;
3 Here we are considering the pulse compression scheme but only one cryomodule  needed only 25MW power but 4us.
From PSI on the BOC: apparently they have a dedicated cooling water group. In their case with a rep. rate of 100Hz they need input flow rate of 102l/min that in our case becomes, divided by 10, ~10l/min! Can we guarantee the regulation with a dedicated chiller air condensed?
Water distribution for magnets is in Linac tunnel  That is not in the budget of Pinj distribution: how much is it available from there?

## Slide 8: S-Band: Phase 1
2028-2029
load
GUN
Isolator under SF6
IP
pen
valve
DC
20-25 MW
1.5ms, 4Hz
S-band
RF Window SF6-Vacuum
RF Window Vacuum-SF6
DC
~30 MW
1.5ms, 4Hz
S-band
Defl. Cavity
load
GUN
Isolator under SF6
IP
pen
valve
DC
RF Window: Vacuum/SF6
RF Window or whole under SF6?
Power Splitter (~10dB)
DC
…
DC
Atten
Ph.
Shift
load
load
Switch
DC?
C-Band Installation
Phase 1a: no def. cav.
Phase 1b: with def. cav.
NB: Def. Cavity not needed for Phase 2. S-Band installation layout for Phase 2  Phase 1a.

## Slide 9: Power splitting scheme to feed the deflecting cavity: no need of an additional isolator
In case of reflection from the Defl. Cavity, because of the presence of the splitter itself, the power reflected back to the klystron is 1/S^2 = 1/100 ==> if i consider Pklys=Pgun+Pcav~30MW, Pref_from_gun~ 300kW (~2.7MW will go to the load in "line" with the RF gun).
Which is line on what the klystron may tolerate in reflection (VSWR~1.2 (max 1.4) in normal operation ==>~20dB return loss==> Pref~350kW).
30 MW
1.5ms, 4Hz
S-band
Pin
Load
Defl. Cavity
RF Gun
Splitter Splitt. Fact. S
27MW
3MW
In case of full ref.
In case of full ref.
So far we are considering for the def. cavity same working parameters (voltage, power) as at SPARC. In case, from detailed calculations, this isn’t the case and Pref>>300kW we can derive the line for the def. cavity after the isolator. Same splitting scheme.

## Slide 10: C-Band: Phase 1
load
C3 1m struct
C3 1m struct
DC
DC
C3 1m struct
25 MW
4ms, 10Hz
C-band
Planar hybrid
Atten
Ph.
Shift
Atten
BOC
PrefAv=210W
PKlysAv=1008W
PBOCAv=575W
PdissAv=365W
Considering a margin of 30% additional power for waveguide losses.
2028-2029

## Slide 11: Components needed for Phase 1 (End of 2028)
 | Components | Comments
Waveguides x C-Band | BOC | 
 | C-Band Load (?) | 50MW peak power, 210W average Power (we may use the same as in Phase 0)
Waveguides x S-Band (Phase 1a) | Isolator+Load | Leadtime 9-10 months. Price 76kEuros  CFT time to be considered
 | RF Windows SF6-Vacuum | 
 | 2 x Dir. Coupler | 
Waveguides x S-Band (Phase 1b) | Isolator+Load | Leadtime 9-10 months. Price 76kEuros  CFT time to be considered
 | RF Windows SF6-Vacuum | 
 | 4 x Dir. Coupler | 
 | Attenuator | 
 | Phase shifter | 
 | RF Switch | 
 | Power splitter - 10 dB 4-ports | 
 | 2 x RF Load S-Band | 3MW peak, 200W average power (not a detailed calculation)
Vacuum x S-Band | IP+Gauges+cables+electronics+… | 
Of course we need also the waveguides but w/o drawings we can’t fix the layout.

## Slide 12: Phase 2
 | 2030 |  |  |  |  |  |  |  | 
 | COLD – Phase 2: 300MeV beam acceleration |  |  |  |  |  |  |  | 
 | Isolator: 3.5l/min | S-RF Unit: 91l/min | Load Isolator: 5l/min (<0.38kW) | C-RF Unit: 123l/min | C-Load: 2x<0.5l/min (2x210W) | C-RF Wind.: 1x3l/min | Dipoles: 1.5l/min (1.04kW) | Solenoid: 5l/min (10kW) | +Def. Cavity1 Load(s): 5l/min (<0.15kW)
Tot | RF~226.5 (+10 for BOC) l/min + Magn.=6.5 l/min & 11.04kW (Def Cav  +5l/min & +0.15kW) NB: All quads will be air cooled |  | (3.5+113+5+123+24+12+25.6+6+5)l/min & 26.3kW (+5l/min & 0.15kW) |  |  |  |  |  | 
From PSI on the BOC: apparently they have a dedicated exchanger. In their case with a rep. rate of 100Hz they need input flow rate of 102l/min that in our case becomes, divided by 10, ~10l/min! Can we guarantee the regulation with a dedicated chiller air condensed?
Water distribution for magnets is in Linac tunnel  That is not in the budget of Pinj distribution: how much is it available from there?
1 In this phase we shouldn’t need a deflecting cavity

## Slide 13: C-Band: Phase 2
50 MW
4ms, 10Hz
C-band
BOC
3dB Splitter
PBOCAv=1.15kW
Considering a margin of 30% additional power for waveguide losses.
Pref, Pload, Pdiss remain the same as Phase 1 (25MW per branch)
2030

## Slide 14
 | Components | Comments
Waveguides x C-Band | 3 dB Splitter C-Band | 
 | C-Band Load | 50MW peak power, 210W average Power (probably we can buy it directly it during phase 0 or 1)
 | 2 x Dir. Coupler C-Band | 
 | Phase shifter | 
 | Attenuators | 
 | Planar Hybrid | 
Components needed for Phase 2 (End of 2029)
Of course we need also the waveguides but w/o drawings we can’t fix the layout. Delay for delivery at least 6 months if we don’t need complicated pieces (twists, particular bends…)

## Slide 15: In addition
C-Band RF Unit CFT3690 launched:
  Writing Tech Specs, dispatch date 19th March 2026;
  Bid submission deadline 20th April 2026;
  Estimated Contract date 29th June 2026;
  Estimated Delivery date 30th June 2027.
LLRF COD Position:
  49 applications received, shortlist defined, first round of video interview soon for a preliminary selection;
  In person (possibly) interviews will follow.