## Slide 1
ASD Workshop - January 24th, 2023
2023 Accelerator Control Activities
Nicolas Leclercq
on behalf of the Accelerator Control Unit

## Slide 2: Outlines
1
Evolution of the Staff
Highlights from 2022
Some Perspectives for 2023

## Slide 3: Evolution of the STAFF
Bye
Welcome
2
Arthur Valiente
left mid. October 2022
Candidate Selected
Wait and see…
🤝
👋

## Slide 4: Highlights 2022
Refurbishment of the {Magnets, Power Supplies} Ecosystem
      Motivations
        ensure long term maintenance
        enhance com. with hardware units and interaction between software components
        enhance performances & ergonomics
      Expected Added Value
        maintainability, extendibility & flexibility (e.g, local/specific magnetic config.)
        ergonomics: change optics params. while the slow orbit feedback (a.k.a., autocor) is running
        performances: allow simultaneous autocor correction in both H & V plane + increase corr. frequency
      Constraints
        modify/test software components representing 22% of the control system
        (4800 Tango devices among the +26500 running in the control system)
        … without impacting the daily operation of the machine!
        sentenced to do better than the previous design/implementation (V1)
      How to Achieve these Goals
        leverage knowledge acquired while developing V1 (learning while doing), manage risk
        promote offline development & validation → major role played by the (enhanced) EBS simulator
        optimize online tests → dedicated installation/rollback tool for MDT sessions
3

## Slide 5: Highlights 2022
Refurbishment of the {Magnets, Power Supplies} Ecosystem
      Status
        magnets part done – in production since Oct. 2022 → the major change is validated!
        significative progress on power supplies & HSM (hot swap manager) control
      Actual Added Value (list validated by Beam Dyn. :-)
        cleaner design = enhanced maintainability
        faster autocor loop: 1 correction every 30s → every 12s (today) → every 3s (near future)
        ability to change sextupole settings while autocor is on
        `→ ability to optimize the lattice in USM-like conditions (or, if necessary, in USM)
        ability to load new “design optics” without impact on the beam (bug fix by design)
        much faster response and visualization of the magnetic strengths modifications
        better integration of the calibration data provided by IDM for each magnet
        simpler cycling of a single magnet (the cycling is a parallel task of the project, more to come)
        enhanced EBS simulator (virtual PS + cycling)
        more to come (e.g., simultaneous autocor correction in both H & V plane)
      Contributions
        involved groups: Beam Dyn., Diags, PSG, IDM, MachOp, ISDD-DEG-EU, ISDD-SWG-ACU
        main ACU contributors: Jean-Luc Pons, Arthur Valiente, Nicolas Tappret, Faranguiss Poncet
3

## Slide 6: Highlights 2022
Transfer of the pre-EBS Data to HDB
      as agreed, Damien Lacoste (HDB/TimeScale DB expert) …
      … migrated 1.4 To from former Oracle & Casandra HDB to a dedicated Timescale DB
        jlauncher → Moni/HDB → pre-EBS Historical Database [1997 – 2018]
      oldest data from 01/05/1997
3

## Slide 7: Highlights 2022
Transfer of the pre-EBS Data to HDB
3
      concatenation of 2 decades of vacuum data from pre & post EBS SR - courtesy of Hugo Pedroso Marques

## Slide 8: Highlights 2022
About HDB
      grew by 1To in 2022
        manageable so far
        10To of disk space remaining on the new cluster
      2.9To of EBS data + 1.4To of pre-EBS data
        separated databases due to major changes in naming schema between pre & post EBS
      we might need to redefine the way we store and use the HDB data
        might be a subtask of a wider data logging project for EBS…
3

## Slide 9: Highlights 2022
ACU CI/CD platform
      ACU internal project
      CI/CD: stands for Continuous Integration / Continuous Delivery
        belongs to the DevOps toolbox
      Life cycle management of our +500 Tango classes and +110 Java applications
        long term maintenance of our code base
        deal with evolution of operating systems, languages/compilers, dependencies (libraries), etc.
        fight against orphan projects & frozen binaries
        control system made of homogenous software components
      Status
        CI part done for C++ projects
        `→ device servers are now aggregation of Tango classes compiled as shared libraries
        `→ allows system wide fixes and enhancements (mutualization)
        `→ allows mass compilation
        we are ready to migrate our +500 Tango classes to Tango 9.4!
      ACU contributors
        Arnaud Le Meillour, Damien Lacoste, Reynald Bourtembourg, Nicolas Leclercq
3

## Slide 10: Highlights 2022
First web app. deployed in the CTRM
      A dashboard on top of the (new) beam killer Tango device
      A jupyter notebook (python) converted into a web application using Voilà
      a POC related to our reflection on the future of the GUIs (see perspectives for 2023)
3
      a Firefox tab rendering the Beam Killer dashboard - courtesy of Lee Carver

## Slide 11: Highlights 2022
Upgrading the Machine Status web page
      the underlying technology obsolete
        Jyse (supplier no longer exists)
      backend by ISDD-SWG-ACU
        bridge to Tango
        done, to validate
      frontend by ISDD-SWG-DAU
        GUI (dashboard)
        in progress
      part of our reflection on the future of our GUIs
        pure web app
        based on specific techs (e.g., React)
3

## Slide 12: Perspectives for 2023
Finalize the refurbishment the Magnets/PS ecosystem (Beam Dyn., PSG)
      autocor + {HSM, Comeca Statum} + cycling
Integration of the 352 MHz SSA (RF)
      ready, waiting for dev. platform from JEMA (control interface)
Extension of the FOFB to 320 BPMs (DIAGs)
      main idea: add the Spark units to the FOFB
      already working (functionally speaking) some remaining tasks for ACU & Diags
Contribute to Inj. Perturbations Studies (Beam Dyn., DIAGs, MachOp)
      e.g., finalize emittance measurement sync. with 4Hz inj. signal
        in production since 01/2023, auto-gain sporadic pb. to be fixed, recently proved to be of interest
      more to come…
4

## Slide 13: Perspectives for 2023
Progress in our reflection on the future of our GUIs
      TAURUS workshop at the ESRF on March 7th & 8th 2023
        part of Tango SIG workshops series
        feedback & strategy for the future – talks by both operation & computing teams
        please visit https://indico.esrf.fr/event/76
Launch a series of discussions about “large scale data logging”
      prerequisite for any (modern) data-driven tools & services
        e.g., machine studies, advanced post-mortem analysis, AI-based models (datasets), etc.
      brainstorming meetings → interest, needs, means & cost… worth it?
        → yes → 📄 proposal → official project
        → no →🗑️
      several aspects: hardware, software, infrastructure → services
4

## Slide 14: Perspectives for 2023
and obviously…
      maintain a strong involvement in the development and the governance of
      continue to support the daily operation of EBS
        for non-trivial requests: meet the ACU team members, brainstorm, agree on what to do…
        … then put the outcomes (specs) of your exchanges in a… Jira ticket!
        ` specs to validation follow-up & traceability
        each ASD group can create as many tickets as necessary but please …
        … provide us with visibility on the 2 “current priorities” using the dedicated flag
4
😱

## Slide 15: Perspectives for 2023
and obviously…
      maintain a strong involvement in the development and the governance of
      continue to support the daily operation of EBS
        for non-trivial requests: meet the ACU team members, brainstorm, agree on what to do…
        … then put the outcomes (specs) of your exchanges in a… Jira ticket!
        ` specs to validation follow-up & traceability
        each ASD group can create as many tickets as necessary but please …
        … provide us with visibility on the 2 “current priorities” using the dedicated flag
4
😱

## Slide 16: Conclusion
ACU is aligned with the strategic objectives of the ESRF ( )
      we are consolidating the EBS control system
        enhance (fixes & new features), industrialize (reliability)
        leverage knowledge, (when needed) dare to change or transform to ensure long term maintainability
…while having a look to the future
      stay tuned, look around, visit & talk to peers, join/animate tech. communities
5
🤓

## Slide 17: On BEHALF of ACU, THANKS for YOUR ATTENTION!
5