## Slide 1: SOLEIL UI experience, … and future plans P.MADELA, G.ABEILLE, R.GIRARDOT, YM.ABIVEN

## Slide 2: Outline
Towards SOLEIL II
UI status around control system
UI organization
Future plans

## Slide 3: Towards SOLEIL II

## Slide 4: SOLEIL in a nutshell
Storage ring 354m, 2.75GeV
29 beamlines
From far IR to hard X-rays
Open to external users in 2008
~ 450 staff members
in 2022
~ 2746 single users
(~150 remote access)
More than
12 000
users since
2008
Notes: Soleil is a synchrotron radiation facility located near Paris in France
The facility uses a circular accelerator to generate extremely bright beams of light
The beams of lights are used for a wide range of scientific research, including physics, chemistry, biology, and materials science.
The facility has 29 beamlines with a wide range of experimental stations.
The experimental stations including imaging, diffraction, and spectroscopy, which enable scientists to study a variety of materials and phenomena.
The synchrotron radiation produced at Soleil covers a broad spectrum, ranging from infrared to X-rays.
It was opened to external users in 2008

## Slide 5: Operation
Beam delivery 24 hours, 7 days a week
5019 h (x 29!) ~ 145000 hours of beamtime in 2022
Beam availability 98,95% in 2022
Mean time between failures (MTBF) 139 hours in 2022

## Slide 6: SOLEIL Upgrade
Better performances for Accelerator and photon sources
  Reaching an emittance < 100 pm.rad.
  Keeping the same electron beam energy : 2.75 GeV
  Preserving a maximum current of 500 mA
  in the multibunch mode.
Upgrade Timeline (1 year delay from initial planning)
< 10 mm x 10 mm
Beam SIZES
Brightness
New access mode with more efficient use of the SOLEIL Beamline
Green infrastructure
  Reduction in the facility
  environmental footprint
  Lower power and water
  consumption
  Reduce operational cost

## Slide 7: Operational organization
Software in operation
  459 c++ Devices
  32 Java Devices
  44 GUI / API
  300 Embeded codes for motion, DAQ, Robotic, PLC
Chart: services requests
| MACHINE | MARS | ANATOMIX | METROLOGIE | CRISTAL | GALAXIES | SAMBA | NANOSCOPIUM | TEMPO | DIFFABS | PSICHE | SIRIUS | SIXS | DEIMOS | ANTARES | PUMA | PX2 | SEXTANTS | DET | SWING | LUCIA | PROXIMA 1 | SMIS | ODE | PLEIADES | CASSIOPEE | AILES | ROCK | DETECTEUR | HERMES
Electronic | 21 | 12 | 11 | 13 | 6 | 6 | 10 | 9 | 9 | 6 | 8 | 7 | 7 | 6 | 2 | 4 | 6 | 7 | 6 | 4 | 1 | 3 | 5 | 2 | 4 | 3 | 2 | 2 | 1 | 1
Computing | 5 | 7 | 5 | 6 | 6 | 2 | 1 | 1 | 3 | 1 | 2 | 2 | 2 | 5 | 3 | 1 | 2 | 4 | 2 | 2
Chart: Incidents profile
| 2018 | 2019 | 2020 | 2021 | 2022
Electronic | 265 | 292 | 210 | 213 | 183
Computing | 472 | 479 | 468 | 474 | 388
Acquisition and Control System Engineering (ISAC) team,
in charge of
  Accelerators and beamlines control systems
  ~12000 Electronics devices (motion, cPCI, PLC, Robotics, …
  ~24000 Tango devices and ~12000 device servers
  Involved in daily operation with 3 on-call duty 24/7:
    Software
    DaQ and motion control
    PLC, Robotic
Involve in TDR around 50 WBS for
  Accelerators program
  Infrastructure Program
  BeamLine and Laboratory (BL2) program
  IT and Data management (transverse to support the others program)
Works with other computing teams for SOLEIL IT systems integration
  ISI: Infrastructure & networks
  ISG: Management Information System
  GRADES: Data analysis

## Slide 8: UI status around control system

## Slide 9: What is your control system made of?
Tango has become a SOLEIL standard de-facto
  Tango is used on all control systems (Accelerators, Beamlines and Labs)
Client
Process, Calculation: Beamline energy…
HW set: insertion, monochromator…
Hardware: motors, power supplies…
Client
Strategy to integrate everything in Tango devices (ancestor of SOA/µService architecture?):
  Hardware (motors, vacuum, power supplies, …)
  Hardware sets (insertions devices, monochromators,…)
  External systems (Building Management in OPC, LINAC in LabVIEW….)
  Calculations, orchestration, workflows (beamline energy, beamline acquisitions processes, experimental data management, archiving…)
Outcomes:
  A seamless integration in all Tango clients (GUIs), in archiving…
  Built-in data correlation
  Autonomy to our users with Tango client API (Python, Matlab, Labview, Igor Pro)

## Slide 10: Comete Framework
For its common GUIs, SOLEIL use Java SWING language and has developed the Comete framework.
Library of widgets and data sources, with intermediates that manage the connection in between.
This framework enables to quickly develop new GUI.

## Slide 11: SCADA Coox
No-code tool to create GUIs with drag & drop.
Developed in Java 8 by ORDINAL company
Based on Comete wigdets
Used by almost all beamlines which are autonomous in creating their views
Builder
  Creation of views by drag’n’drop
  (uses SOLEIL’s components with Comete)
Viewer
  Runs the views previously created with Builder

## Slide 12: Common GUIs
v
Detectors
Tango Archiving
Alarms - PANIC
Acquisition
Experimental data recording
Tango tools
Large usage of ATKPanel, ATKTuning, Jive, Astor, ATKTrend
Multi Channel Analyzer
Configure & plot
HDB & TDB & Snap
Spyc: SOLEIL Python CLI
Fronts for scan devices
(FlyScan & ScanServer)
Configure & plot
Beam image calculations
All the Java GUI based on Comete are also beans that can be integrated into COOX screens

## Slide 13: Accelerators GUIs
Beam positions - Matlab
Beam Nu/WaveNumber measure - Labview
Postmortem analysis - Labview
PSS permits (Personal Safety System)- Labview
Utilities monitoring (AC & Fluids) - Labview
Beam purity measure - Python

## Slide 14: Apps for web evaluation
HDB
accelerators
Machine
Status
Machine status
Grafana
GraphQL backend to archiving

## Slide 15: UI Organization

## Slide 16: Accelerators practices
Accelerators staff develop their own scripts/devices/GUI
  LabView, maintained by operators, acc. groups
  Matlab, maintained by physicists
  Python (TkInter, scripts, Tango devices), maintained by operators, physicists and acc. groups
GUI apps that embed the process are critical
  Top-up Injection process (Labview)
  Some feedbacks (Slow orbit feedback, …) (Matlab) …
Lots of accelerators' GUI are only for experts, and not for operations
    152 LabVIEW apps
    56 Python apps
    114 Matlab apps
    60 Grafana dashboards
Accelerators as owner of
Labview apps
Python apps
Matlab apps
Accelerators as user of
Tango GUI (Jive, ATK…)
PANIC
Databrowser
Mambo / Bensikin
MachineStatus
Grafana (under evaluation)

## Slide 17: Beamlines practices
Beamline staff develops their own scripts/devices/GUI
  Python (TkInter, scripts, Tango devices)
  On a few beamlines and laboratories
    Igor Pro,
    LabVIEW
    Matlab
Beamline staff creates and maintains views of COOX synoptics
Beamlines as owner of
Python apps
Igor Pro apps
Labview apps
Beamlines as user of
Tango GUI (Jive, ATK…)
PANIC
COOX
Salsa / FlyScan GUIs
Datastorage/Databrowser
Mambo/Bensikin
MachineStatus

## Slide 18: Computing teams practices
Computing teams provide common GUI solutions (Comete, COOX, Tango binding)
  Development, delivery, deployment, training and support
  Computing teams provide a very limited support for Matlab, Labview, Python and Igor Pro
  Provides help for deployment of these products, their licenses and their tango bindings
Resources for GUI (not fulltime)
  ISAC :
    1 expert for Java Swing GUI development
    1 expert for back-end in Java
    1 expert for front in React.JS
  ISI:
    1 sys. admin for products and licenses installation, OS upgrades
Computing teams as owner of
Tango generic GUI (Jive…)
Comete framework
GUI based on Comete
PANIC
COOX
Spyc
Tango Bindings
Grafana (under evaluation)
Support on deployment of products (Matlab,Labview,Python…)
Tango
Nexus

## Slide 19: Who is responsible for the development and the maintenance of the GUIs?
Accelerators
Beamlines
Computing teams
Accelerators as owner of
Labview apps
Python apps
Matlab apps
Accelerators as user of
Tango GUI (Jive, ATK…)
PANIC
Databrowser
Mambo / Bensikin
MachineStatus
Grafana (under evaluation)
Computing teams as owner of
Tango generic GUI (Jive…)
Comete framework
GUI based on Comete
PANIC
COOX
Spyc
Tango Bindings
Grafana (under evaluation)
Support on deployment of products (Matlab,Labview,Python…)
Tango
Nexus
Beamlines as owner of
Python apps
Igor Pro apps
Labview apps
Beamlines as user of
Tango GUI (Jive, ATK…)
PANIC
COOX
Salsa / FlyScan GUIs
Datastorage/Databrowser
Mambo/Bensikin
MachineStatus

## Slide 20: Feedbacks
Feedbacks on user autonomy
  Positive feedbacks from users of COOX and apps w/ Tango bindings
  First feedbacks w/ Grafana are also positive
Sharing concerns between computing teams and business teams difficult to balance :
  Computing teams: focus on stability and reliability
  Business teams: focus on flexibly and changes
  Long term maintainability to be build :
    Migration from Python 2 to Python 3 is in progress with a support of ISAC on Beamlines and Accelerators
  At some point, IT expertise is mandatory to operate GUI applications as they interact with a lot of IT components (Tango devices, the OS, network….)

## Slide 21: Future plans

## Slide 22: Future strategy
Transversal TDR program has a project dedicated to UI just started
  Strategy definition is under construction in the IT & Data management program
  Accelerators, beamlines and computing teams working together on the project
UI requirements
  Shared development between business & computing teams
  Well-known technologies are important -> Possibility to sub-contract
  Existing framework with a strong community to be able to share experience /dev
  Control layer between Tango device servers & GUI:
    Add security/authentication: to allow only approved clients
    Add requests tracking: to track clients requests and abnormal usage
UI short/mid term perspectives:
  Maintain existing Java Swing
  Organize transition to new GUI technologies
  Deploy Grafana for monitoring on the control systems
  Provide Python ecosystem
Accelerators & Beamlines requests:
  Python/PyQt and other Python packages
  Web solutions
Computing teams & business teams work together to share the strategy

## Slide 23: Expectations from the workshop
Understanding organization in the other institutes
  Who do what? How?
  Experience of migrating to new GUI technologies: skills, complexity
  What about long-term maintenance of the GUI? Which policy did you choose?
  UX Expertise?
Understanding operational architecture up to the desktop
  Cloud technology approach
  What about security for these upcoming solutions?
  What about library packaging?
  How to transition smoothly?
Feedbacks about Taurus
  Users’ feedbacks from other institutes
  Which skills required to provide and deliver Taurus?
  Technical feedbacks: complexity, maintainability

## Slide 24: Conclusion
GUI strategy under construction in the context of SOLEIL II TDR
Current challenge is to manage the transition
Balance between desktop and web to be defined
Looking for partners to share UI frameworks and experiences
Architecture and technology Transformation
complexity/reliability/maintenability
Collaboration
Strong community
Robustness
Flexibility