## Slide 1: Variable
Any scalar parameter acting on a lattice
Can act on simulations or real equipment
Can be used for
  Matching
  Response matrix analysis and corrections
Methods
  Variable.set(lattice, value)
  value = Variable.get(lattice)
  Variable.increment(lattice, value)
  …
Properties
  history
  initial_value
  last_value
  previous_value
  …

## Slide 2: Variables in simulation
Variable(setfun, getfun, name, bounds,…) Generic variable: getfun(lattice) and getfun(lattice, value) can do anything.
  ElementVariable(refpts, attrname, index, name, …) Apply the same scalar value to any attribute of selected elements of the lattice. Not yet implemented: a user-defined function could act on several elements. Ex.: when given refpts=[n-1, n, n+1], it could shift longitudinally the element n by modifying the drifts n-1 and n+1

## Slide 3: VariableList
Allow vectorized access to a list of variables
Methods:
  VariableList.set(lattice, values)
  values = VariableList.get(lattice)
  VariableList.increment(lattice, values)
  …