## Slide 1: Python AT for Accelerator Controls
Martin Gaughran, Diamond Light Source

## Slide 2: Background

## Slide 3: Accelerator Tools
High-Level Applications team is part of Accelerator Controls
We are responsible for several accelerator tools, including:
  Top-up process
  Slow Feedbacks
Transitioning some tools away from Accelerator Physics for HLA support:
  Beam-Based Alignment (soon!)

## Slide 4: MATLAB Middle Layer (MML)
Used at Diamond by Accelerator Physics and Operations
Simulation or direct control
Includes generic tools and utilities
Currently used at Diamond for:
  Beam-based alignment
  Chromaticity and dispersion
  Response matrix calculations
  Etc.
G. Portmann, J. Corbett, A. Terebilo, “An Accelerator Control Middle Layer using MATLAB”, Proceedings of 2005 Particle Accelerator Conference, 2005

## Slide 5: Migration to Python
Diamond intends to move tools critical to user operations away from Matlab:
  Improved support from Controls group
  Better programming language
  Easier to integrate with other Controls tools
  Etc.
Interest in a more uniform approach to Python development

## Slide 6: Python Tools

## Slide 7: Pytac
Python Toolkit for Accelerator Controls
Work with standard Lattice elements similar to pyAT
  Load elements from MML configuration
Customise Control System backend for EPICS support
Physics / engineering unit conversions

## Slide 8: Pytac interface
Machine hardware
IOC
S01.get_value('b2’, pytac.RB, pytac.PHYS, pytac.LIVE)
S03.set_value('b2', value, pytac.SP, pytac.PHYS, pytac.LIVE)
IOC
CA
CA

## Slide 9: ATIP
Accelerator Toolbox Interface for Pytac
Provides a simulator to Pytac, using pyAT
Enables offline testing of accelerator controls applications

## Slide 10: ATIP interface
Accelerator Toolbox simulation
S01.get_value('b2’, pytac.RB, pytac.PHYS, pytac.SIM)
S03.set_value('b2', value, pytac.SP, pytac.PHYS, pytac.SIM)

## Slide 11: Virtual Accelerator (Virtac)
Standalone application with EPICS interface.
EPICS backend to Pytac is then able to interact with the Virtac
  Complete end-to-end simulation of our high-level Controls applications
Virtual accelerator can be used with non-pytac commands by including extensions

## Slide 12: Virtac interface
Virtual Accelerator
S01.get_value('b2’, pytac.RB, pytac.PHYS, pytac.LIVE)
S03.set_value('b2', value, pytac.SP, pytac.PHYS, pytac.LIVE)
IOC
CA
CA

## Slide 13: Virtual Accelerator (design)
ATSimulator provided by ATIP library
ATIPServer designed for Virtac
pythonSoftIOC used for EPICS IOC generation
Tobyn Nicholls

## Slide 14: Python tools overview
Pytac can be used for the majority of tasks
Direct EPICS control required for non-standard components

## Slide 15: Adoption at Diamond

## Slide 16: Slow Feedbacks
Python IOC
Uses Pytac for majority of features
Includes:
  Slow orbit feedback
  RF feedback
  Tune feedback
  Vertical emittance feedback
Virtual Accelerator is used for offline testing

## Slide 17: Beam-Based Alignment (BBA)
Python ‘Slow’ and ‘Fast’ Beam-Based Alignment developed in 2023
Uses Pytac for control of lattice components
Intend to add Virtac support for testing ‘slow’ BBA
Joshua Appleby, Development of Fast Beam-Based Alignment for Diamond Light Source, 2023

## Slide 18: Fast Beam-Based Alignment
Priority for our BBA development
Process developed by ALBA
No simulator support due to non-standard components, e.g. :
  Fast archiver
  Corrector oscillation control
Uses unit and integration tests
Joshua Appleby, Development of Fast Beam-Based Alignment for Diamond Light Source, 2023

## Slide 19: Near-term Improvements
Improve design of Virtac extensions for customisability
Provide standard pattern for integration of facility-specific components with Pytac
Adopt modern Python features
  Type hints problematic due to cothread – use different EPICS library

## Slide 20: Summary
Pytac & Friends
Only supports EPICS
Matlab Middle Layer
Supports EPICS and Tango
Feedback systems, tools etc. available for anyone
Wide collaboration
Supports Accelerator Toolbox
No generic tools and utilities
Only maintained by Diamond Light Source
Supports Accelerator Toolbox

## Slide 21: Repositories and Documentation
https://github.com/DiamondLightSource/pytac
https://github.com/dls-controls/atip
  Includes ATIP and Virtual Accelerator
  Will be moved soon to DiamondLightSource

## Slide 22: Acknowledgements
Will Rogers, Razvan Vasile
  Pytac, Slow Feedbacks
Tobyn Nicholls
  ATIP, Virtual Accelerator
Joshua Appleby
  FBBA

## Slide 23: Demo

## Slide 24: Any Questions?