## Slide 1
AT with GPU tracking
J-L Pons

## Slide 2: CUDA evaluation
cudaAT is designed with the aim to be 100% compatible with AT
No modification required in existing AT scripts
cudaAT is written in c
nvcc compiler (nvidia c compiler)
Very very first release (only basic pass implemented)
DriftPass
BndMPoleSymplectic4Pass
StrMPoleSymplectic4Pass
6D tracking benchmark
cudaAT benchmark will be presented with a constant longitudinal momentum but calculation are done
No synchrotron radiation
No RF cavity
It is an evaluation, not an acted decision

## Slide 3: TEST LATTICE
Benchmarking will be presented using the AT primer lattice
(10 slices per magnet)
QF=at.Quadrupole('QF',0.5,1.2)
Dr = at.Drift('Dr', 0.5)
HalfDr = at.Drift('Dr2', 0.25)
QD = at.Quadrupole('QD', 0.5, -1.2)
Bend = at.Dipole('Bend', 1, 2*math.pi/40)
FODOcell = at.Lattice([HalfDr, Bend, Dr, QF, Dr, Bend, Dr, QD, HalfDr],
name='Simple FODO cell', energy=1E9)
SF = at.Sextupole('SF', 0.1, 0)
SD = at.Sextupole('SD', 0.1, 0)
drs = at.Drift('DRS', 0.2)
FODOcellSext = FODOcell.copy()
FODOcellSext[6:7] = [drs,SD,drs]
FODOcellSext[2:3] = [drs,SF,drs]
FODOSext = FODOcellSext*20
# Tune sextu
refsext = at.get_cells(FODOSext, at.checktype(at.Sextupole)) # Select all sextpoles
refsf,refsd = np.flatnonzero(refsext)[:2]
at.fit_chrom(FODOSext, refsf, refsd, [0.5, 0.5])

## Slide 4: Dynamic APERTURE of FODO with SEXTUPOLE
DA (512x512) on H100
[262144 particle, 1000 turns]
at_pass loop: 824 ms
ap_pass loop (same grid): 57915 ms on 128 cores (AMD EPYC 7542 32-Core Processor 3.0 GHz)
1 x H100 ~ 70 x 128 core hosts
H100 is the latest NVIDIA product Amazing performances

## Slide 5: ERROR (EMULATED FP64 on GeForce GTX 1050 Ti)
Error is the maximum of abs(cudaAT – cpuAT) for 256 particles tracked inside the DA (for non linear)

## Slide 6: ERROR (NATIVE FP64 on H100)
Error is the maximum of abs(cudaAT – cpuAT) for 256 particles tracked inside the DA (for non linear)
Slight difference between emulated and native FP64 GPU (can be seen only on the non linear lattice) The error over 10.000 turns is not catastrophic compare to CPU for this basic lattice For a real light source, FP128 can be emulated in case of failure

## Slide 7: BENCHMARKING
UFO has been configured to execute the same number of kick/drift than cudaAT
(30 slices in UFO)
(10 slices in cudaAT)
UFO is still ~2.5 times faster, but why ?

## Slide 8: Dynamic code generation (UFO)
x -= 0.0;
y -= 0.0;
x += px * (0.1 * 1.0 / 2.);
y += py * (0.1 * 1.0 / 2.);
px -= ((0.*0.1 * 1.0/1) * oodppo + (((0.*0.1 * 1.0/1) * oodppo + (((0. + 5.6)*0.1 * 1.0/1) * oodppo * x - (0. * y)) / 2) * x - ((((0. + 5.6)*0.1 * 1.0/1) * oodppo * y + (0. * x)) / 2 * y)) / 1);
py += (((0.*0.1 * 1.0/1) * oodppo + (((0. + 5.6)*0.1 * 1.0/1) * oodppo * x - (0. * y)) / 2) * y + ((((0. + 5.6)*0.1 * 1.0/1) * oodppo * y + (0. * x)) / 2 * x)) / 1;
px -= x * ((0) * (0) * (0.1 * 1.0)/1 / (0.1 * 1.0) / (0.1 * 1.0));
x += px * (0.1 * 1.0 / 2.);
y += py * (0.1 * 1.0 / 2.);
x -= -(0.0);
y -= -(0.0);
sf: SEXTUPOLE, L = 0.1, K2 = 5.6;
RING: LINE = (sf);
1 slice
The compiler will automatically skip all useless operations and generate a fast code

## Slide 9: PERFORMANCES
Symplectic integrator (kind of 4th order integrator used in AT)
Most of the time is spent inside the polynomial evaluation (there are often lots of zeros)
for (i=max_order-1; i>=0; i--) {
ReSumTemp = ReSum*r[0] - ImSum*r[2] + B[i];
ImSum = ImSum*r[0] + ReSum*r[2] + A[i];
ReSum = ReSumTemp;
}
Unrolling polynomial by dynamic code generation (as done in UFO) and adding new parameters to AT can really help to increase performance and fit better to user needs, for instance:
DesignPolynomA, DesignPolynomB (coefficients can be moved to faster constant R/O memory) ErrorPolynomA, ErrorPolynomB for spreading errors
PolynomA = DesignPolynomA[:] + ErrorPolynomA[:] (trig a fast dynamic recompilation when something is updated)
The polynomials can even be multidimensional allowing tracking one single particle (or more) in multiple ring (parallel response matrix calculation, parallel tune scan)
It should be possible to maintain backward compatibility (at least for pyAT)

## Slide 10: COLLECTIVE EFFECTS
No evaluation there but
Very fast shared memory can allow to build histograms
used for WakeFields
__shared__ _FLOAT sr6[GPU_GRID * 6];
sr6[0 + threadIdx.x * 6] = _r6[0]; // x
sr6[1 + threadIdx.x * 6] = _r6[1]; // px/p0 = x'(1+d)
sr6[2 + threadIdx.x * 6] = _r6[2]; // y
sr6[3 + threadIdx.x * 6] = _r6[3]; // py/p0 = y'(1+d)
sr6[4 + threadIdx.x * 6] = _r6[4]; // d = (pz-p0)/p0
sr6[5 + threadIdx.x * 6] = _r6[5]; // c.tau (time lag)
_FLOAT* r6 = &sr6[0 + threadIdx.x * 6];
At the hardware level parallelization is done by bunch of 128 particles
When well synchronized, it allows efficient SIMD and SIMT
Lots of possibility to implement thread barriers (or fences) in CUDA
Breaking the ring and going back to host has no significant
impact if the number of tracked particles is a multiple of the number of cuda cores.

## Slide 11: CUDA and COMPUTE CAPABILITIES
{0x20, 32}, // Fermi
{0x21, 48}, // Fermi
{0x30, 192}, // Kepler
{0x32, 192}, // Kepler
{0x35, 192}, // Kepler
{0x37, 192}, // Kepler
{0x50, 128}, // Maxwell
{0x52, 128}, // Maxwell
{0x53, 128}, // Maxwell
{0x60, 64}, // Pascal
{0x61, 128}, // Volta
{0x62, 128}, // Volta
{0x70, 64}, // Turing
{0x72, 64}, // Turing
{0x75, 64}, // Turing
{0x80, 64}, // Ampere
{0x86, 128}, // Ampere
{0x87, 128}, // Ampere
{0x89, 128}, // Ampere
{0x90, 128}, // Hopper
GTX 1050 Ti 6x128 => 768 cuda cores
A40 88x128 => 10752 cuda cores
A100 (cluster busy)
H100 114x128 => 14592 cuda cores
Stream processor and thread spawning
If threads are well spawned and synchronized a single H100 cuda core is roughly 60% of a 3.0GHz CPU !
Hardware Version
Number of StreamProcessors
Number of MultiProcessors

## Slide 12: COTATION

## Slide 13: CUDA / OPENCL
CUDA is a professional API (NVIDIA)
Lots of parameters specific to nvidia boards can be tuned to increase performances
Coalesced memory has not yet been implemented in cudaAT
Very accurate and complete documentation
Good error reporting and diagnostic tools
Free
OPENCL
Support all GPU trademark
Open community
Due to multi trademark support, some features are not present
Free

## Slide 14: INSTALATION PROCEDURE / ALTERNATIVE
pip / setuptools does not support native cuda extension (nvcc) 
NVCRT
NVIDIA RunTime compiler, it uses the default c/c++ compiler
OpenCL C/C++
Open GPU RunTime compiler, also uses default c/c++ compiler
pyopencl
OpenCL python binding
Need to rewrite at.c in python
what about matlab ?
cuda-python
Low level python NVCRT binding supported by nvidia
What about matlab ?

## Slide 15: THANKS
Beam Dynamics Group (ESRF)
Technical Infrastructure Division (ESRF)
Michele Carlà (ALBA)